## Slide 1: WF on NB-IoT DL carrier frequency determination in in-band operation mode
Huawei, HiSilicon, …
R1-16xxxx
3GPP TSG RAN WG1 #84
St Julian’s, Malta, 15th-19th February, 2016
Agenda item 7.2.1.1.4

## Slide 2: Proposals
Before RRC connection, the UE only expects NB-PSS/SSS in PRBs which satisfy the following:
  The maximum offset from the LTE channel raster to the center frequency of an NB-IoT carrier which transmits NB-PSS/SSS is no more than 7.5 kHz
  NB-PSS/SSS of an NB-IoT carrier is aligned to a PRB indexed by nRB in in-band operation mode
    The set of nRB consists of LTE PRB indices in the following Table (starting from 0) on the next slide

## Slide 3
LTE system bandwidth | 3MHz | 5MHz | 10MHz | 15MHz | 20MHz
PRB indices for NB-PSS/SSS transmission | 2, 12 | 2, 7, 17, 22 | 4, 9, 14, 19, 30, 35, 40, 45 | 2, 7, 12, 17, 22, 27, 32, 42, 47, 52, 57, 62, 67, 72 | 4, 9, 14, 19, 24, 29, 34, 39, 44, 55, 60, 65, 70, 75, 80, 85, 90, 95