## Slide 1: WF on >6GHz Channel Modeling Scenarios
NTT DOCOMO, AT&T, ALU, ASB, CATT, Deutsche Telekom, Ericsson, ETRI, Fraunhofer, Huawei, HiSilicon, Intel, InterDigital, KT, LGE, NEC, Mitsubishi, Nokia, NTT, Qualcomm, Samsung, Sharp, Sony, Vodafone
R1-161145
3GPP TSG RAN1#84
St Julian’s, Malta, Feb. 15 - 19, 2016
Agenda Item: 7.3.5.1

## Slide 2: Proposal
Scenarios for >6GHz channel modeling are as follows.
  UMi – street canyon
    Urban micro cell with outdoor and indoor UEs.
    BS antenna is placed below rooftop level of surrounding buildings.
  UMi – open square
    Urban micro cell with:
      Outdoor UEs in the open square
      Outdoor and indoor UEs outside of the open square
    BS antenna is placed below rooftop level of surrounding buildings. BS antenna can be placed at surrounding buildings or inside of the open square, e.g., lamppost.
    Width of the open square is in the order of 50 to 100 m.
    Note: A subset of features comprising this scenario can be applicable for Stadium case.
  UMa
    Urban macro cell with outdoor and indoor UEs.
    BS antenna is placed at or above rooftop level of surrounding buildings.

## Slide 3: Proposal
Scenarios for >6GHz channel modeling are as follows (Cont.)
  Indoor – office
    Sub scenario 1 – Open office: Typical open office environment with cubicles, chairs, etc.
    Sub scenario 2 – Mixed office: Typical office environment with open cubicle areas, meeting rooms, walled offices, corridors, etc.
    We utilize common modeling methodologies and parameterization, unless separate modeling is identified as necessary.
    Following features are separately modeled.
      LOS probability
      FFS: other features
    BS antenna is placed at ceiling.
  Indoor – shopping mall
    Large multiple-story building with open ceiling in the middle. Shops are arranged along the outer wall of the building.
    BS antenna is placed at ceiling. Details FFS.

## Slide 4: Proposal
Following scenarios are the 1st priority.
  UMi – street canyon
  Indoor – office
  UMa
Other scenarios are the 2nd priority.