## Slide 1: WF on starting subframe of MPDCCH SS
CATT, NEC, Panasonic
R1-161401
3GPP TSG RAN WG1 Meeting #84
St Julian’s, Malta, 15th – 19th February 2016
Agenda item 7.1.5

## Slide 2: Background
For MPDCCH UE-specific search space, and Type0-MPDCCH common search space, the starting subframes are given by ,
where
- T=Rmax*G, G is from {1, 2, 3, 4, 5, 8, 10, reserved} at least for FDD (For TDD, may re-consider) and the index of one element is given by the higher layer parameter mPDCCH-startSF-UESS.

## Slide 3: Proposal
G is from {2, 4, 5, 8, 10, 20, 40, reserved} for TDD
The starting subframe of Type1-MPDCCH CSS is derived using the same mechanism as that for MPDCCH USS and Type0-MPDCCH CSS:
  Replace mPDCCH-startSF-UESS to mpdcch-startSF-CSS-RA-r13.