## Slide 1: WF on remaining details on NB-IoT uplink frame design
Huawei, HiSilicon, Nokia
R1-161441
3GPP TSG RAN WG1 #84
St Julian’s, Malta, 15th-19th February, 2016
Agenda item 7.2.1.2.1

## Slide 2: Background
For 15kHz subcarrier spacing, OFDM/SC-FDMA symbol boundary is no change from LTE
At least for FDD with the normal CP case,
  For 3.75kHz subcarrier spacing of uplink,
    Define a 2ms NB-slot, there are 7 symbols.
    One symbol consists of [FFS] Ts of symbol with CP length of [FFS] Ts assuming Ts=1/1.92MHz. Editor will take care how to capture Ts value in the spec.
    The above symbols are located from the beginning of 2ms period. FFS the usage of the remaining time in the NB-slot if there is the remaining time
    The 2ms NB-slot boundary is aligned with LTE subframe boundary. FFS among odd only or even only or to support both even/odd
    FFS on collision of LTE SRS for in band mode
      Opt 1: eNB scheduling or implementation
      Opt 2: puncture/rate matching of 3.75kHz transmission to avoid the collision
      Opt 3: define a GP to avoid potential collision
      Note combination of above options can also be considered.

## Slide 3: Proposal 1
For 3.75kHz subcarrier spacing of uplink,
  One NB-IoT symbol consists of 528Ts of symbol with CP length of 16Ts assuming Ts=1/1.92MHz.
  Besides the seven symbols located from the beginning of 2ms period, the remaining time (144Ts) is used as a guard period to minimize the collision between NB-IoT symbols and LTE SRS;

## Slide 4: Proposal 2
NB-IoT configuration field regarding the avoidance of LTE SRS is broadcasted in the NB-IoT system information
  The 3.75kHz NB-Slot boundary is configured to align with either even or odd LTE subframe so that most of the LTE SRS positions are protected by 3.75kHz NB-IoT Guard Period.
For LTE SRS symbol positions that are not able to align with GPs in NB-Slot, the overlapped NB-IoT symbols are not used and rate matching is used for avoidance of collision with LTE SRS
The same density of DMRS in LTE is used for 3.75 kHz PUSCH and the DMRS pattern is shifted by one symbol (i.e. DMRS on the third or fifth symbol in NB-Slot) to avoid the collision between DMRS and LTE SRS