## Slide 1: Way Forward on clarification of number of symbols used in PRACH
Ericsson Huawei, HiSilicon
3GPP TSG RAN WG1 Meeting #84
St. Julian’s, Malta, 15th - 19th February 2016
Agenda item 7.2.1.2.2
R1-161444

## Slide 2: Background
Agreements:
NB-PRACH uses a subcarrier spacing of 3.75kHz
2 CP lengths are provided to support different cell sizes
  66.7 us and 266.7 us
Hopping is between groups of 6 symbols
  Details of hopping pattern FFS
First level fixed size hopping is used between 1st/2nd and between 3rd/4th symbol groups
Second level hopping is used between 2nd/3rd symbol groups:
  Details of 2nd level hopping FFS till Friday (e.g. based on LTE PUSCH type 2 hopping or fixed hopping)

## Slide 3: Confusion in the agreements
Agreements:
2 CP lengths are provided to support different cell sizes
  66.7 us and 266.7 us
Hopping is between groups of 6 symbols
  Details of hopping pattern FFS
Potential confusion:
  6 symbols only applies to a CP length of 266.7 us
  For 66.7 us CP, it is actually 5 symbol and a CP

## Slide 4: Proposal
Hopping is between groups of 6 symbols
  Details of hopping pattern FFS
Hopping is between groups
  CP length of 266.7 us, a group is defined as 5 symbols and a CP of length of 266.7 us
  CP length of 66.7 us, a group is defined as 5 symbols and a CP of length of 66.7 us
  Other group size for high doppler support is not precluded