## Slide 1: WF on correlation distance for spatial consistency in RMa
Intel, Ericsson, AT&T, ETRI, Huawei, HiSilicon, KT Corporation, Nokia, NTT DOCOMO, Qualcomm, Samsung
R1-165233
3GPP TSG RAN1 #85
Nanjing, China, May 23 - 27, 2016
Agenda Item: 7.2.3.2

## Slide 2: Background
Spatial consistency modelling has been agreed in R1-163475/R1-161726
RMa is agreed in the last day of RAN1 #84b meeting
The correlation distance for spatial consistency modelling in RMa is missing

## Slide 3: Proposal
  The correlation distance for cluster/ray specific random variables for RMa is according to the table below
  The correlation distance for LoS state is [60m] for RMa
 | RMa | 
 | LOS | NLOS
Correlation distance (m) for cluster/ray specific random variables | [50] | [60]