## Slide 1: WF on frequency-dependent LSPs
Ericsson, Telstra, [...]
R1-165480
3GPP TSG RAN WG1 Meeting #85
Nanjing, China, May 23-27, 2016
Agenda Item: 7.2.2

## Slide 2: Background
The current agreements and working assumptions have many frequency-dependent LSPs with values in square brackets
  E.g. on the form LSPx = A*log10(1+f)+B
These frequency dependencies are hotly contested, see e.g. R1-164732 in support of frequency dependence and R1-165351 in support of frequency-independent LSPs
For InH, a compromise solution has been proposed in R1-165461
  The solution is to replace A by A/2
  Frequency-dependence is thereby halved
  However, it was noted that this compromise also changed the mean value over the frequency of interest
  To preserve the LSP value at 6 GHz, also the B parameter should be modified as follows:
    B_new = B+(A-A_new)*log10(7)
    with A_new = A/2 this becomes
    B_new = B+A/2*log10(7)

## Slide 3: Background
The following figure illustrates the problem with only changing A and how the proposed solution addresses this

## Slide 4: Proposal
Proposal 1: Use the compromise solution between frequency-dependent and frequency-independent for all scenarios
  All LSPs on the form
    LSPx = A*log10(1+f)+B
  are changed to
    LSPx = A/2*log10(1+f)+B+A/2*log10(7)
  This is applied to all currently frequency-dependent LSPs

## Slide 5: Background
The consistency of the new channel model with the < 6 GHz 3D SCM and IMT-Adv is a major concern
  Some LSPs in the new model may behave very differently below 6 GHz than 3D SCM or IMT-Adv
  This is a cause of concern for many companies and is currently blocking the discussions on the validity range for the new model
UMa vs 3D SCM:
  Path loss models are fully consistent (3D SCM was reused)
  LSPs are almost fully consistent: LSP value at 6 GHz equals 3D SCM value
RMa vs IMT-Adv
  Path loss models and LSPs are fully consistent (IMT-Adv was reused)
InH vs IMT-Adv
  Path loss models are not consistent
  LSPs are partially consistent (some changed, some reused)
UMi vs 3D-SCM
  Path loss models are not consistent (~7 dB discontinuity at 6 GHz in NLOS)
  LSPs are partially consistent (some changed, some reused)

## Slide 6: Background
One solution is to modify the LSP behavior in the new model such that the value at 6 GHz equals the legacy value
  By modifying the frequency-dependent or constant values
This allows the new and legacy models to be used in parallel, or alternatively the new model can replace the legacy models
  Previous simulation results will not be changed
  NR simulations of below and above 6 GHz will be consistent
For frequency-dependent LSPs on the form LSPx = A*log10(1+f)+B this can be achieved by changing B such that
  Bnew = LSPlegacy - A*log10(1+6)
  and also mandating that LSP(f<6 GHz) = LSP(6 GHz)
For frequency-independent LSPs, the legacy values can be reused

## Slide 7: Proposal
Proposal 2: Change the frequency-dependent LSPs such that the value at 6 GHz equals the legacy value, and mandate that the LSP value is constant below 6 GHz
Proposal 3: Change frequency-independent LSPs to the legacy values

## Slide 8: Summary
Proposal 1: Use the compromise solution between frequency-dependent and frequency-independent for all scenarios
  All LSPs on the form
    LSPx = A*log10(1+f)+B
  are changed to
    LSPx = A/2*log10(1+f)+B+A/2*log10(7)
  This is applied to all currently frequency-dependent LSPs
Proposal 2: Change the frequency-dependent LSPs such that the value at 6 GHz equals the legacy value, and mandate that the LSP value is constant below 6 GHz
Proposal 3: Change frequency-independent LSPs to the legacy values