## Slide 1: WF on evaluation assumptions for high speed train scenario: Macro + relay at 30GHz
Mitsubishi Electric, ETRI
3GPP TSG RAN WG1 Meeting #85 R1-165484 Nanjing, China, 23th - 27th May 2016
Agenda item: 7.1.2

## Slide 2: Background
In R1-163887, option 2 alt. 2 (Macro + relay nodes) is agreed to be included in evaluation
More clarifications and detailed evaluation parameters are needed.

## Slide 3: Proposal
Linear RRH placement along the rail track
Macro + relay nodes (agreed in R1-163887) :
  Alt. 2: For BS to relay: Around 30 GHz
  For relay to UE: Around 30 GHz or Around 70 GHz or Around 4 GHz
Example of a set of parameters is provided in page 4-7
  Other set of parameter values can be considered
Unidirectional beam and bidirectional beam can be considered

## Slide 4: Proposal
SFN scenario parameters (Option 2, Alt. 2)
Parameter | Value
Distance between RRH and Railway track | 5m
Distance between RRH | As illustrated in slide 6
Num of RRHs connected to one BBU | 3
Height of RRH | 2.5m

## Slide 5: Proposal
non-SFN scenario parameters (Option 2, Alt. 2)
Parameter | Value
Distance between RRH and Railway track (from RRH to middle of track) | 5m
Distance between RRH | As illustrated in slide 7
Num of RRHs connected to one BBU | 3
Height of RRH | 2.5m

## Slide 6: Proposal
SFN model (Option 2, Alt. 2)
6m
3.38m
580m
580m
5m
1732m
BBU
BBU
BBU
RRH1
RRH2
RRH3
RRH1
RRH2
RRH3
RRH1
RRH2
RRH3
572m

## Slide 7: Proposal
Non-SFN model (Option 2, Alt. 2)
6m
3.38m
580m
580m
5m
1732m
BBU
BBU
BBU
RRH1
RRH2
RRH3
RRH1
RRH2
RRH3
RRH1
RRH2
RRH3
572m
Different RRH identity

## Slide 8: Proposal
Other evaluation parameters
Parameter | Value
Train length | 400m
Num of users per train | 1000
Channel model | 5G channel model

## Slide 9: Proposal
KPI
  Mobility
link level evaluation is recommended
  SFN as in page 6
  non-SFN as in page 7
NR RAN1 technologies that need to consider high speed impact for RRH to relay link
  Numerology, MIMO