## Slide 1: WF on URLLC KPIs and Evaluation
Qualcomm Incorporated
3GPP TSG RAN WG1 #85 R1-165487
Nanjing, China, May 23 - 28, 2016
Agenda item: 7.1.2

## Slide 2: URLLC KPI’s
URLLC latency and reliability KPIs are define in conjunction
  (Latency, Reliability) of (L, R) is met if packet is delivered within L ms U-plane latency with packet error rate < R.
  E.g., (1ms, 1e-5)
URLLC capacity is defined as delivered traffic given the (L, R) constraint
  Denoted as C(L,R)
URLLC/ eMBB multiplexing capacity is defined as the simultaneously delivered URLLC capacity C(L,R) and eMBB capacity T

## Slide 3: Evaluation Assumptions
Proposal 1: Single URLLC traffic model should be used evaluate URLLC KPIs
  Example: Fixed packet size of 32 Bytes, Poisson arrival rate of ,
  Example: single directional and bi-directional traffic could be considered
Proposal 2: Latency metric should capture transmission latency, processing latency, retransmission latency and queuing/scheduling latency
Proposal 3: Link level BLER evaluation should include control and data channels
  With and without other cell interference
Proposal 4: System level evaluation should capture other cell interferences