## Slide 1: WF for TRP Antenna Modeling
3GPP TSG RAN WG1 Meeting #85 R1-165488
Nanjing, China, May 23 – 28, 2016
Samsung, Intel, Ericsson
Agenda item 7.1.2

## Slide 2: Background
700MHz: Up to 64 Tx /Rx antenna elements
4GHz: Up to 256 Tx /Rx antenna elements
30GHz: Up to 256 Tx /Rx antenna elements;
  [84b-13 agreement] Continue discussion whether to increase the number of antenna elements.
70GHz: Up to 256 Tx /Rx antenna elements
  [84b-13 agreement] Up to 1024 Tx /Rx antenna elements
Parameter | Values
Antenna element vertical radiation pattern (dB) | 
Antenna element horizontal radiation pattern (dB) | 
Combining method for 3D antenna element pattern (dB) | 
Maximum directional gain of an antenna element GE,max | 9 dBi
Parameter | Values
Antenna element vertical radiation pattern (dB) | 
Antenna element horizontal radiation pattern (dB) | 
Combining method for 3D antenna element pattern (dB) | 
Maximum directional gain of an antenna element GE,max | 9 dBi
TRP Tx power:
For 100 MHz BW @ 30 GHz:
Indoor: 23 dBm,
Dense-urban: Macro [40] dBm / Micro 35 dBm,
UMa: 43 dBm
For 100 MHz BW @ 70 GHz:
Indoor: 23 dBm
TRP noise figure:
7 dB for the above 6GHz

## Slide 3: Proposals
Proposal 1: For evaluation, consider the following antenna configurations:
At 4GHz:
Dense urban and Urban macro
– Baseline: (M,N,P,Mg,Ng) = (8,16,2,1,1), (dV,dH) = (0.8, 0.5)λ.
– Other configurations to be further discussed for each feature to be evaluated
• Indoor hotspot:
– FFS
At 30GHz:
• Dense urban and Urban macro:
– Baseline: (M,N,P,Mg,Ng) = (4,8,2,2,2). (dV,dH) = (0.8, 0.5)λ. (dg,V,dg,H) = ([12.4], [4])λ.
– Other configurations to be further discussed for each feature to be evaluated
• Indoor hotspot:
– FFS
At 70GHz:
• Dense urban:
– Baseline: (M,N,P,Mg,Ng) = (8,16,2,4,4). (dV,dH) = (0.5, 0.5)λ. (dg,V,dg,H) = ([4.0], [8.0]) λ.
– Other configurations to be further discussed for each feature to be evaluated
• Indoor hotspot:
– FFS

## Slide 4: Proposals
  Proposal 2: Consider the following a TXRU to antenna elements mapping as examples
  At 4GHz: the same as TR36.897
  At 30GHz and 70GHz:
    Option 1: a single TXRU is mapped per panel per polarization.
    Option 2: a single TXRU is mapped per panel per subarray per polarization,
      E.g., where a subarray consists of consecutive M/2 vertical antennas and N/2 horizontal antennas with the same polarization.
      Other subarray configurations are not precluded.
    Fully connected TXRU mapping is not precluded.
  Proposal 3: For multi beam based approaches evaluations for 30GHz and 70GHz, consider the following:
  TXRU to antenna mapping weights are adjustable and used to steer the panel beam direction in multi beam based approaches in time domain.
  Companies should describe TXRU mapping weights for the panel beams
  Consider the following as two examples for constructing mapping weights:
    Example 1: Kroneker products of two oversampled DFT vectors, with O1 and O2 oversampling factors for the two dimensions.
      Companies can choose O1, O2 and also beam scanning range reduction along with their results.
    Example 2: Beam broadening weights
    Other weights are not precluded. E.g, weights with finite resolution.