## Slide 1
Way Forward on sPUCCH design
LG Electronics, Ericsson , Panasonic, NTT DOCOMO, Sharp, KDDI
R1-165544
3GPP TSG RAN WG1 Meeting #85
Nanjing, China 23rd - 27th May 2016
Agenda item 6.2.10.1

## Slide 2
The following sPUCCH formats are recommended to be supported
  One sPUCCH format for HARQ-ACK and/or SR feedback for a serving cell
  sPUCCH format(s) for multiple HARQ-ACK bits, e.g. as in CA and frame structure type 2
    The amount of sPUCCH formats to support is depending on the maximum identified payload size to support
    sPUCCH format allows for multiplexing of HARQ-ACK and SR
    FFS: sPUCCH format supports CSI feedback
  Design principles for sPUCCH
    Intra-TTI frequency hopping is recommended to be supported
      FFS: 2OS or 3OS sPUCCH depending on feasibility to support intra-TTI frequency hopping
    Aim to reuse aspects of existing PUCCH formats in the design
Proposal