## Slide 1: WF on ZoD offset for Indoor office
Huawei, HiSilicon, AT&T, Ericsson, Intel, Nokia, NTT DOCOMO, Samsung
R1-165569
3GPP TSG RAN WG1 Meeting #85
Nanjing, China, 23 - 27 May, 2016
Agenda Item: 7.2.2

## Slide 2: Background
In current TP in R1-164609. The ZoD offset value for indoor office is still N/A.
To facilitate the channel model calibration and future key technologies evaluation, it is necessary to provide the parameterization results for ZoD offset for indoor office.
Considering the influence of ZoD offset on indoor office scenario can be ignored, it can be treated as 0 for both LOS and NLOS cases.

## Slide 3: Proposal
The ZoD offset for indoor office can be set as 0 for both LOS and NLOS cases
Table 7.5-9: ZSD and ZoD offset parameters for RMa and Indoor-office (part)
Scenarios |  | Indoor-Office | 
 |  | LOS | NLOS
ZoD spread (σZSD) log10([]) | µZSD | [-1.43*log10(1+f)+2.25] | 1.37
 | ZSD | [0.13*log10(1+f)+0.15] | 0.38
ZoD offset | µoffset,ZOD | 0 | 0
f is carrier frequency in GHz; d2D is MS-BS distance in m. |  |  |