## Slide 1: WF on Scenarios for Multiple Access
ZTE, ZTE Microelectronics, InterDigital, Qualcomm Inc., Spreadtrum
R1-165595
3GPP TSG RAN WG1 #85 meeting
Nanjing, China, 23rd – 27th May 2016
Agenda item 7.1.3.2

## Slide 2: Background
Agreement made in RAN1#84bis.
  Non-orthogonal multiple access should be investigated for diversified NR usage scenarios and use cases
  At least for UL mMTC, autonomous/grant-free/contention based non-orthogonal multiple access should be studied

## Slide 3: Proposals (1)
Autonomous/grant-free/contention based UL non-orthogonal multiple access has the following characteristics
  A transmission from UE does not need the dynamic and explicit scheduling grant from eNB
  Each time in transmission, a UE randomly chooses a code/sequence or a pattern of interleaver from a pool known to eNB and UE before hand
  Multiple UEs can share the same time and frequency resources

## Slide 4: Proposals (2)
For autonomous/grant-free/contention based UL non-orthogonal multiple access, the following should be studied
  Collision of code/sequence/interleaver pattern from different UEs but on the same resource
  Potentially relaxed requirement for UL synchronization (DL synchronization assumed)
    Case 1: Timing offsets between UEs are within a cyclic prefix
    Case 2: Timing offsets between UEs can be greater than a cyclic prefix, FFS the exact model of timing offsets
  Potentially relaxed requirement for power control, i.e., no closed-loop
    Case 1: Perfect open-loop power control, i.e., equal average SNR between UEs
    Case 2: Realistic open-loop power control with certain alpha and P0 values
    Case 3: no power control