## Slide 1: Evaluation of TBCC and Polar Codes for Small Block Lengths
Huawei, HiSilicon
3GPP TSG RAN WG1 #85 meeting
Nanjing, China, 23rd – 27th May 2016
Agenda item 7.1.5.1
R1-165599

## Slide 2
- Performance Calibration
  Polar performance calibration
    QUP[1,2] is used to calibrate the polar performance in R1- 164356.
  TBCC(R1-164356) performance evaluation
    Different numbers of initial states LVA for TBCC have been evaluated to find the performance bound.
    Enhanced TBCC in R1-164356 has been evaluated
- CRC error detection for list decoding
  Miss detection issue of CRC-Aid list decoding for Polar and TBCC has been investigated
In this contribution, we evaluate the performance for Polar code and TBCC for mMTC/URLLC and compare with results in R1-164356. The two aspects below are addressed.

## Slide 3
Performance Calibration

## Slide 4
Calibration of R1- 164356 “Performance Evaluation of TBCC and Polar Codes Fig. 1”,
LTE TBCC: K = 29 info. bits +16 CRC bits, N = 288, native R=1/3, QPSK
  HW Polar QUP: K = 29 info. bits +16 CRC bits, N = 288, cSNR = 2 dB, QPSK, L=32
Fig. 1

## Slide 5
Calibration of R1- 164356 “Performance Evaluation of TBCC and Polar Codes Fig. 4”,
LTE TBCC: R=1/3, info. bits = 20,40,200,600,1000 ; 16 CRC bits, m-LVA32(m ≈ 16 initial states)
  HW Polar QUP: R= 1/3, info. bits = 20,40,200,600,1000; 16 CRC bits, L=32
Fig. 2

## Slide 6
Calibration of R1- 164356 “Performance Evaluation of TBCC and Polar Codes Fig. 4”
LTE TBCC: R=1/3, info. bits = 40; 16 CRC bits, m-LVA32(m =1,16,64 initial states)
  HW Polar QUP: R= 1/3, info. bits = 40 ;16 CRC bits, L=32,256,2048

## Slide 7: Observations
m-LVA was used in R1-164356 (m~16)
Performance bound comparison
  Bound of TBCC LVA32 is the 64-LVA32, when all the initial states of TBCC have been used
  the actual list size is 64*32 = 2048,
  Complexity will be ~1.4 times compared to Polar L2048[3]
Polar outperforms TBCC

## Slide 8
Calibration R1- 164356 “Performance Evaluation of TBCC and Polar Codes Fig. 5”
Enhanced TBCC: K = 29 info. bits +16 CRC bits, N = 288, native R=1/3,1/6, QPSK
  HW Polar QUP: K = 29 info. bits +16 CRC bits, N = 288, cSNR = 2 dB, QPSK, L=32
Fig. 4

## Slide 9: Observations
The complexity of the TBCC (1/6,16-LVA32) is ~2*16*1.4 = 45 times of Polar L=32[6],
  performance is almost the same with polar with LVA32
With similar complexity (Polar uses a larger list), there will be ~0.9 dB gain for Polar Code compared to TBCC VAL[3].
  TBCC has R= ((29+16)/ 288) ≈ 1/6,
  This is the best performance for the enhanced TBCC(R1- 164356 ,proposal 4).

## Slide 10
CRC error detection for list decoding

## Slide 11
We use TBCC M-LVA X and Polar CA-SCL X to investigate how severe the CRC miss detection issue can be, since both these two decoders use CRC to assist decoding.
Channel | AWGN | 
Modulation | QPSK | 
Coding scheme | TBCC | Polar
Decoding algorithm | M-LVA X | CA-SCL X
Info. bits length | 29 bits | 
CRC length | 16 bits | 
Encoded bits length | 288 bits | 

## Slide 12
Polar CA-SCL 2048
Fig. 5a
Fig. 5b

## Slide 13: Observations
For TBCC M-LVA 32 scheme, LTE TBCC is used
  To achieve best performance under this list size setting, all the M=64 possible initial states are searched during the decoding, hence totally 32*64=2048 possible paths are tried for decoding.
For Polar CA-SCL 2048
  The 16 bits CRC is placed at the relatively high reliable position when doing polar channel coding.
  Also the CRC bits could be put at the most reliable bits position in Polar to guarantee the CRC error detection performance than TBCC.
Under these settings:
  TBCC 64-LVA 32 vs. Polar List64, the complexity of TBCC is about 34 times of Polar[3].
  TBCC 64-LVA 32 vs. Polar List2048, the complexity of TBCC is about 1.4 times of Polar[3].

## Slide 14
In Fig. 5a, the BLER for dash curves are calculated by raw info. bits checking result divide total packets, and the BLER for solid curves is calculated by the CRC checking result divide total packets.
In Fig. 5a we can see that there is almost no miss detection issue for Polar CA-SCL 64, and even for Polar CA-SCL 2048, the miss detection issue is very small.
For miss detection caused by CRC-Aid list decoding, Polar is better than TBCC with the same number of possible path.
Note that (both with ~2048 list), the complexity of polar LVA is ~0.7 of that of TBCC, while the gain is ~1.0 dB at BLER=10e-4.
Fig. 5b shows that for Polar code, the output decoded info. bits sequence can be selected out within 1~3 CRC checks rather than going through all the candidate paths(2048 in this example), and the corresponding miss detection degradation is negligible as shown in Fig.5a.

## Slide 15
Conclusion
Observation 1: Polar code outperforms LTE TBCC and Enhanced TBCC(R1-164356,proposal 4.).
Observation 2: There is no severe miss detection issue for Polar CA-SCL decoding.
Proposal 1: To achieve high performance and high reliability, Polar code should be employed in control channel, mMTC and uRLLC scenario.

## Slide 16
Reference:
K. Niu and K. Chen, "Beyond turbo codes: Rate-Compatible punctured polar codes," in Proc. of IEEE ICC'13, Budapest, Hungary, June 2013.
R1-164039, “Polar Codes: Encoding and Decoding”, Huawei, HiSilicon
R1-164040, “On latency and complexity of Polar Codes”, Huawei, HiSilicon
R1-164356, “Performance Evaluation of TBCC and Polar Codes”, Ericsson

## Slide 17
Appendix

## Slide 18: The complexity computation[3]
Polar
  A SCL decoder has a total computational complexity of O(L*N*log2(N)) + O(L*(N-1) ) + K* O(2*L*log2(2*L))
  With L=64, N=512, K=45, the complexity is about 367936
  With L=2048, N=512, K=45, the complexity is about 12695552
TBCC
  A LVA decoder with all intial states search has a computational complexity of S*(K*O(2*S*L+16) + K*S*L)
  With S=64,K=45,L=32, the complexity is about 17740800
TBCC 64-LVA 32 / Polar L64 ~= 17740800/ 367936 ~= 34
TBCC 64-LVA 32 / Polar L2048 ~= 17740800/12695552 ~= 1.4