## Slide 1: WF on Implicit Dependencies Assumptions
InterDigital, Ericsson, Huawei, HiSilicon
3GPP TSG RAN WG1 #85 R1-165607
Nanjing, China
23rd – 27th May 2016
Agenda item: 7.1.1
Document for decision

## Slide 2: Background
In LTE, a number of implicit (i.e. non-configurable) dependencies exist between signals, e.g.:
  Most transmissions depend on PCI determined from PSS/SSS
  Relative timing of PDSCH/PUSCH transmission and corresponding HARQ A/N
  QCL assumption between CRS and DM-RS (pre-R11 releases)
  PUCCH resource for HARQ-ACK depend on starting CCE of PDCCH containing assignment
Such implicit dependencies tend to complicate introduction of new features, i.e. forward compatibility

## Slide 3: Proposal
  Implicit (i.e. non-configurable) dependencies between transmissions that exist in LTE design are not by default assumed to be introduced in NR design.
  An identity parameter may tie signals for search/synchronization (e.g. PSS/SSS) to the broadcast transmission of essential system information (e.g. MIB)
    Name of identity parameter TBD (e.g. cell ID, hypercell ID, system ID)
    Other dependencies to this identity parameter can be introduced if considered beneficial taking into account forward compatibility, signalling overhead and complexity