## Slide 1: Way Forward on longer CP for MBSFN
Ericsson, Qualcomm, BBC, EBU
R1-165610
3GPP TSG RAN WG1 Meeting #85
Nanjing, China, 23rd - 27th May 2016
Agenda item 6.2.5.1

## Slide 2: Proposal
  MBSFN subframes with numerology characterised by OFDM core symbol duration of >=400us and CP>=100us shall be supported
  FFS whether OFDM core symbol duration of 800us and CP>100us shall be supported
    For 800us MBSFN core symbol duration, the unicast control symbols of the same subframe puncture (shorten) the MBSFN symbol CP
  FFS whether OFDM core symbol duration of 266us and CP=66us shall be supported
  Numerologies that span across subframe or radio frame boundaries are not supported.
  For objective (a), existing signalling enables restricting legacy UEs to only make MBMS MDT measurements on subframes with the legacy cyclic prefix by using different MBSFN areas for legacy UEs and Rel-14 UEs