## Slide 1: Way Forward on SLS evaluation assumptions
LG Electronics, …
3GPP TSG RAN WG1 #85
Nanjing, China, 23rd – 27th May 2016
Agenda item 7.1.2
R1-16xxxx

## Slide 2: Background
Agreements on evaluation metrics for SLS made in RAN1 #84bis meeting captured from R1-163560 are as follows :
  For SLS, the following are used as evaluation metrics
    eMBB: TRP spectrum efficiency and 5th percentile user spectrum efficiency; user experienced data rate and area traffic capacity; signaling overhead
    mMTC: Connection density with “connection efficiency” reported; latency for infrequent small packets; signaling overhead
    URLLC: Reliability for a target latency
However, it is not so clear that the definition of the evaluation metrics for mMTC/URLLC and how they fit in the SLS

## Slide 3: Proposal
For SLS in RAN1, the following are used as evaluation metrics
  eMBB: TRP spectrum efficiency and 5th percentile user spectrum efficiency; user experienced data rate and area traffic capacity; signaling overhead
  mMTC: Connection density with “connection efficiency” reported; latency for infrequent small packets; signaling overhead as defined follows :
    Connection efficiency = TRP spectrum efficiency / (packet arrival rate * average packet size per UE)
    FFS for other metrics above
  URLLC: Reliability for a target latency
    Clear definition of “reliability for a target latency” is needed for RAN1 evaluation purpose
  FFS additional metrics