## Slide 1: Way Forward on Channel Coding Scheme for New Radio
Samsung, Nokia, Qualcomm, Intel, ZTE
3GPP TSG RAN WG1 #85 meeting
Nanjing, China, 23rd – 27th May 2016
Agenda item 7.1.5.1
R1-165637

## Slide 2: Proposal
Take the following as conclusion for RAN1#85
  All candidate channel coding schemes for eMBB application show comparable link performance in most cases
  Observations on LTE turbo code for high code rates
    LTE turbo code requires higher decoder computational complexity compared to LDPC code
    LDPC code is superior to LTE turbo code in terms of latency and high data throughput
  LTE turbo code starts generating error floor between BLER=10-2 and 10-3 for high code rates and for some large information block lengths (e.g. some sizes ≥1000 bits)
  LDPC code can be designed to meet the flexibility required for application scenarios in NR systems