## Slide 1: WF on NPDCCH ordered PRACH
Ericsson
R1-165652
3GPP TSG RAN WG1 meeting #84bis
Nanjing, China,23rd-27th May, 2016
Agenda item 6.1.6

## Slide 2: Background
At RAN1#84bis the following is agreed regarding NPDCCH ordered PRACH in NB-IoT,
PDCCH order
  NB-PDCCH order is carried in format N1
  1 bit field indicates NB-PDCCH order
  The starting number of NPRACH repetitions is included (2 bits)
  The remaining bits in DCI format N1 are set to ‘1’.
Observation: The current agreed NPDCCH ordered PRACH brings in more problems than benefits to the network, as there is no adequate information at the eNB for the network to benefit from the NPDCCH ordered PRACH (see R1-165355).

## Slide 3: Proposal 1
Introduce the tone index in DCI format N1 for the NPDCCH ordered PRACH.

## Slide 4: Proposal 2
    A field of 6 bits in DCI format N1 should be used to indicate the tone index as
      Indicate the absolute tone index.
      The tone index in DCI format N1 has to indicate a tone in a PRACH resource matching the PRACH repetitions.
      A tone outside the PRACH region is not allowed.