## Slide 1: WF on time reference of ACK/NACK of NPDSCH
Huawei, HiSilicon, CATT, Intel, Panasonic, u-blox, ZTE, Samsung, China Unicom, Astri, NEUL, CATR
R1-165664
3GPP TSG RAN WG1#85 meeting
Nanjing, China, May 23-27, 2016
Agenda item 6.1.6

## Slide 2: Background(1)
In RAN1#84bis, the following was agreed:
  ACK/NACK Resource Indication
    In DCI format N1, ACK/NACK Resource Indication: 4 bits
  Fixed baseline subcarrier, and
    3.75kHz: 3 bits for frequency allocation, 1 bit for time allocation
      Starts from subcarrier 45, and offset grows negatively
        Offset values are {0, -1, -2, -3, -4, -5, -6, -7}
      Time offset is 0,1 x 8ms
    15kHz: 2 bits for frequency allocation, 2 bit for time allocation
      Starts from subcarrier zero, and offset grows positively
        Offset values are {0, 1, 2, 3}
      Time offset is 0,1,2,3 x 2ms
  Repetition
    The predefined set of numbers of repetition for ACK/NACK resource unit is {1, 2, 4, 8, 16, 32, 64, 128}

## Slide 3: Background(2)
Regarding the time reference point of ACK/NACK over which the time offset is applied, two alternatives were discussed in the email discussion[84b-03]:
Alt. 1:
  Baseline time point for time domain allocation of A/N transmission:
  A/N transmission is relative to the first time reference point which is at least 12 ms later than the end of NPDSCH
  The period of the time reference point is fixed to X ms.
    X = 2
    The start of the period is from (SFN#0, subframe#0).
Alt. 2:
  Baseline time point for time domain allocation of A/N transmission:
  A/N transmission is relative to the first time reference point which is at least 12 ms later than the end of NPDSCH
  The period of the time reference point is fixed to X ms.
    X = 1
    The start of the period is from (SFN#0, subframe#0).

## Slide 4: Proposal
Baseline time point for time domain allocation of A/N transmission:
  A/N transmission is relative to the first time reference point which is at least 12 ms later than the end of NPDSCH
  The period of the time reference point is fixed to X ms.
    X = 2
    The start of the period is from (SFN#0, subframe#0).