## Slide 1
3GPP TSG RAN WG1 Meeting #85bis R1-165674
Nanjing, China, 23th - 27th May 2016
Agenda item: 7.1.1
Way forward on forward compatibility for waveform evolution
Spreadtrum, CATR, CMCC, Cohere, Deutsche Telekom, InterDigital, Orange, Sony, Telstra, Telefonica, ZTE

## Slide 2: Background
Agreed:
  Phase 1 and later phases of NR should be designed to ensure forward compatibility and compatibility of different features.
Waveform is a fundamental PHY technology which can essentially impact system performance.
Multiple new waveforms have been proposed as 5G waveform candidates.
Besides existing waveform candidates in NR, other new waveforms would emerge in near future, which may further improve the performance of 5G systems.

## Slide 3: Proposal 1
Forward compatibility for waveform evolution should be ensured in system framework design.
  Downlink, uplink and sidelink share the same framework of physical layer processing as the below figure shows.
Note: Transform precoding can be configured to pre-process the signal using, for example, a DFT-based transform.

## Slide 4: Justification
Transformation may need to be implemented in downlink and sidelink as well as in uplink, according to the following reasons:
  Some kind of DFT-s-OFDM waveform for high frequency, e.g. UW-DFT-s-OFDM (R1-164028, R1-165057), GI DFT-s-OFDM, (R1-164716)
  Special transformation may be needed for specific scenarios, e.g. OTFS (R1-163619)
  Uniform DL/UL/SL waveform may be needed for some cases (e.g. in R1-164047)
  Support of flexible configuration of Air Interface profiles and forward compatibility through Software Defined Air Interface (R1-162867)