## Slide 1: WF on Phase Noise Modeling
Nokia, Alcatel-Lucent Shanghai Bell, NTT DoCoMo, Samsung, Qualcomm, Ericsson, Intel, InterDigital
3GPP TSG RAN WG1 #85 R1-165685
Nanjing, P.R. China
23rd – 27th May 2016
Agenda item: 7.1.2
Document for decision

## Slide 2: Background
The following agreements were made in RAN WG1 meeting #84bis on the subcarrier spacing discussion.
  All companies are requested to analyze/evaluate following aspects
    Realistic phase noise
Phase noise, caused by oscillator implementation, requires specific consideration especially in high carrier frequencies.
Though 11 PN models are proposed or referred in RAN WG1 meeting #85, in order to perform fair evaluation, at least the common principles should be agreed, and limited number of PN models should be considered.

## Slide 3: Proposal
  PN model should be developed for evaluation of NR systems for above 6GHz with the following principles
Proposal #1:
  Phase noise model for UE should be considered for the evaluation by default.
  Implementation cost, complexity and power consumption at the UE should be taken into account.
  The PN modelling in eNB is FFS.
Proposal #2:
  Realistic PN model should consider total oscillator PSD including the impact of reference clock, loop filter noise and VCO sub-components. (e.g. PLL-based model, multi-pole/zero model)
  Each company should provide the model and the parameters used for the evaluation.

## Slide 4: Proposal
Proposal #3:
  The oscillator PSD level increases by 20dBc/Hz per decade of increase of the carrier frequency. (Baseline)
  A different parameter set of phase noise model can be defined for specific target frequency.
Proposal #4:
  Companies are encouraged to provide link level evaluation result with the phase noise model. Following phase noise models are provided as examples.
    UE model in R1-164041
    Proposed WF in R1-165005
    Model A in R1-163984
    mmMagic high and low model
  Other phase noise model is not precluded.
  Companies should provide which phase noise model is applied for the evaluation.

## Slide 5: Example Model
PN Model 1 (R1-164041) : Blue curve @30GHz

## Slide 6: Example Model
PN model 2 (R1-165005) : Black Curve @40GHz

## Slide 7: Example Model
PN model 3 (R1-163984)

## Slide 8: Example Model
mmMagic High(red) and Low (blue) @30GHz
ICT-671650 mmMAGIC project, “Initial multi-node and antenna transmitter and receiver architectures and schemes,” Deliverable D5.1, March 2016, https://bscw.5g-mmmagic.eu/pub/bscw.cgi/d95056/mmMAGIC_D5_1.pdf