## Slide 1: Way forward on mMTC evaluation assumption
Huawei, HiSilicon, […]
3GPP TSG RAN WG1 Meeting #85 R1-165690
Nanjing, China, 23rd – 27th May 2016
Agenda Item: 7.1.2

## Slide 2: Background
In RAN1#84bis, general evaluation assumptions were agreed for indoor hotspot, dense urban, urban macro and rural.
For mMTC, TR38.913 identified “urban coverage for massive connection” as the deployment scenario.
This WF provides general evaluation assumptions for this deployment scenario.

## Slide 3: Proposal
Attributes | Values or assumptions
Layout | Single layer - Macro layer: Hex. Grid
Inter-BS distance | 1732m
Carrier frequency | 700MHz
Aggregated bandwidth | Up to 2MHz (UL+DL)
Simulation bandwidth | Companies report simulation bandwidth used in evaluation
Channel model | 3D UMa Take 5GCM output into account if applicable.
Tx power | BS: 49dBm / 20MHz UE: Max 23dBm
BS antenna configuration | Tx/Rx: 2/4 ports (8 as optional)
BS antenna pattern | Follow the modeling of TR36.873
BS antenna height | 32m
BS antenna tilt | Companies report tilt
BS antenna element gain + connector loss | 8 dBi, with 3dB cable loss
BS receiver noise figure | 5 dB
UE antenna elements | 1Tx, 2Rx 1 Rx is not precluded
UE antenna height | 1.5m
UE antenna gain | -4dBi
UE receiver noise figure | 9dB
Traffic model | Non-full buffer small packet. Consider future trend of mMTC traffic Refer to 3GPP TR45.820; Lower inter-packet arrival time (IPA) compared to TR45.820 needs to be considered Examples: 1/5, 1/10, 1/20 of IPA in TR45.820
UE distribution | 20% of users are outdoor in cars (100km/h) 80% of users are indoor (3km/h) Users dropped uniformly in entire cell
UE receiver | MMSE-IRC as baseline, advanced receiver is not precluded
BS receiver | Advanced receiver could be considered
(NOTE: the red highlights are update from R1-164044)