## Slide 1: WF on UE measurement and reporting
Huawei, HiSilicon, NEC,…
3GPP TSG RAN WG1 Meeting #85
Nanjing, China, 23th - 27th May 2016
AI: 6.2.2.4
R1-165692

## Slide 2: Background
In Europe, ETSI EN 302 571 specifies rules that all UEs need to comply with to operate in the 5855 MHz to 5925MHz unlicensed spectrum.
In this standard, (decentralized) congestion control is currently one mandatory requirement to meet for any ITS technology to operate in this spectrum.
An necessary element to enable congestion control is to measure the channel utilization ratio and perform transmission adaptation if certain criteria are met.
Hence, congestion control should be studied and specified by 3GPP.

## Slide 3: Background
At the RAN WG1 Meeting #84bis, reporting of radio-level measurements of sidelink was discussed. It was decided to continue discussion until RAN WG1 Meeting #85.
Radio-level measurement of sidelink is beneficial to improve accuracy on how far two UEs are apart compared to use of the geo-information. It can also help to decrease the possibility of interference and increase the opportunity of the spatial reuse.

## Slide 4: Proposal
Support radio-level measurements of sidelink
  FFS measurement definition and details
    Example 1: Energy/power measurement of the sidelink bandwidth for channel utilization ratio
    Example 2: measurement of DMRS of SA transmitted from other UEs for their data transmission
Support utilization of radio-level measurement
  UE measurement report to the eNB
  UE measurement made available to the higher layers
    Inform SA2 on this observation