## Slide 1: WF on LBT Priority Class for UL Transmission
Ericsson, [Intel], ZTE, Nokia, Alcatel-Lucent Shanghai Bell
3GPP TSG RAN WG1 #85 R1-165715
Nanjing, China
23rd – 27th May 2016
Agenda item: 6.2.1.5
Document for decision

## Slide 2: Proposal
Rel-14 supports four LBT priority classes for UL transmissions as in the following table.
  Note: CWmin, CWmax, n refer to the minimum CW, maximum CW and the number of consecutive CCA slots in the defer period, respectively.
  Note: the smaller the LBT priority class number, the higher the priority.
FFS: additional set of LBT parameters for the LBT priority classes that can be chosen by the eNB

## Slide 3: Proposal (cont.)
LBT priority class | n | CWmin | CWmax | MCOT | Set of CW sizes
1 | 2 | 3 | 7 | 2 ms | {3,7}
2 | 2 | 7 | 15 | 4 ms | {7,15}
3 | 3 | 15 | 1023 | 6ms (see note 1) or 10 ms (see note 2) | {15,31,63,127,255,511,1023}
4 | 7 | 15 | 1023 | 6ms (see note 1) or 10 ms (see note 2) | {15,31,63,127,255,511,1023}
NOTE 1: The MCOT of 6 ms may be increased to 8 ms by inserting one or more gaps. The minimum duration of a pause shall be 100 µs. The maximum duration (Channel Occupancy) before including any such gap shall be 6 ms. The gap duration is not included in the channel occupancy time. NOTE 2: If the absence of any other technology sharing the carrier can be guaranteed on a long term basis (e.g. by level of regulation), the maximum channel occupancy time (MCOT) for LBT priority classes 3 and 4 is for 10 ms, otherwise, the MCOT for LBT priority classes 3 and 4 is 6ms as in note 1. |  |  |  |  |