## Slide 1: WF on MCOT limit Signaling and Modifying LBT type
Ericsson, [ZTE], [MediaTek], [WILUS]
3GPP TSG RAN WG1 #85 R1-165716
Nanjing, China
23rd – 27th May 2016
Agenda item: 6.2.1.5
Document for decision

## Slide 2: Background
Agreement:
For the DL and UL transmissions occurring on the same channel, an eNB starting the DL transmission based on a Cat 4 LBT with a given MCOT, can share its channel occupancy with its UEs such that the total transmission duration by the eNB and UEs does not exceed the MCOT limit.
  A channel occupancy is started with a DL transmission after CAT4 LBT.
  UL transmissions within a channel occupancy scheduled by a single UL grant or by multiple UL grants shall be contiguous if they can be scheduled contiguously
    Note: If the UL transmissions within a channel occupancy cannot be scheduled contiguously, then there can be gaps between the UL transmissions
    Note: There can be gaps due to LBT failures at the UE between the UL subframes in which transmissions occur
    Note: There can be gaps for 1 or 2 symbols between the scheduled UL subframes within an MCOT
  Any gap between two consecutive transmissions that is larger than 25 µs shall not be counted towards the MCOT limit.
  [Agreement: An LBT based on a 25 µs CCA can be performed for any of the new UL transmission within the MCOT limit.] and shall take place immediately prior to the UL transmission.
    Note: A UE performing Cat. 4 LBT for a new UL transmission as part of the channel occupancy initiated by the eNB is not precluded
  The eNB shall schedule such that the duration of all scheduled transmissions shall be counted towards the MCOT; however the LBT duration is not counted towards the MCOT.
  Within a channel occupancy, any gap between non-consecutive DL transmissions shall be counted towards the MCOT limit.
  FFS multiple transitions between DL and UL within a channel occupancy, and the associated detailed behavior (e.g. allowed gaps and how gaps are counted towards MCOT)
  FFS: Whether scheduling the same UE can be done in non-consecutive or only in consecutive subframes within a channel occupancy
A channel occupancy may be started with a UL transmission after CAT4 LBT by the UE.
No two channel occupancies whether they are initiated by the eNB or initiated by UEs served by the eNB can overlap in time

## Slide 3: Background
An eNB is acquiring the right to access the channel by performing the appropriate procedure. After successfully completing the procedure, a channel occupancy starts and a channel occupancy time (COT) is started to be counted according to the agreed rules.
The channel occupancy may be shared with other UEs based on the agreed rules.
The COT has a limit which is defined as a parameter of the channel access procedure that was used to acquire the channel occupancy. This is the Maximum Channel Occupancy Time (MCOT).
The MCOT doesn’t change over the validity of the channel occupancy. However the remaining channel occupancy time may be reduced over time.
Available or Remaining Channel Occupancy Time (RCOT) is proposed to be signaled in common-PDCCH.

## Slide 4: Background
DL | DL | DL |  |  |  | UL | UL | U | UL | UL
Cat. 4 LBT
A : Tx starting time
after Cat 4 LBT
MCOT= 3 ms
Cat. 4 LBT
RCOT limit=3
RCOT limit=2
RCOT limit=1
DL | DL | DL |  | DL |  | UL | UL | U | UL | UL
B : Tx after Cat 4 LBT
MCOT= 3 ms
Cat. 4 LBT
RCOT limit=4
Trigger 25µs LBT
A : Tx after Cat 4 LBT
MCOT= 3 ms
RCOT limit=3
RCOT limit=2
RCOT limit=1

## Slide 5: Proposal
Remaining COT =x as a non-negative integer is signaled in the C-PDCCH of a DL subframe where RCOT = x in subframe “n” indicates that
  any UL transmission from SF#(n+x) and onwards corresponds to Cat 4 LBT; AND
  any UL transmission after the transmission in SF#n until SF#(n+x-1) can be performed based on CCA of 25 us LBT;
The LBT procedure for any UL subframe in SF#n to SF#(n+x-1) for which the eNB had already indicated to be Cat. 4 LBT, can be switched to an LBT based on 25 µs CCA if an RCOT of value x is detected in C-PDCCH in SF#n.
If UE PUSCH starting symbol is symbol#0, UE prepares PUSCH assuming a starting transmission time. The UE is not expected to change this starting time based on the LBT method used. FFS the start time between the following options:
  Option 1: PUSCH starts at symbol#0
  Option 2: PUSCH starts at 25us after SF boundary
If PUSCH starting symbol#1, UE always prepares PUSCH as it is transmitted from symbol#1.