## Slide 1: Way Forward on differentiate the GNSS timing and eNB timing
3GPP TSG RAN WG1 Meeting #85 R1-165743
Nanjing, China, 23rd – 27th May 2016
Agenda Item: 6.2.2.7
Huawei, HiSilicon, Qualcomm, Samsung, NTT DOCOMO , LG Electronics, Panasonic, Xinwei, ZTE, ITRI, CATR

## Slide 2: Background
SLSS transmitted from out-coverage UE directly synchronized with GNSS or GNSS equivalent with sufficient reliability is differentiated from SLSS_net with in coverage indicator 1
At least reuse priority order SLSS_net with in coverage indicator 1, SLSS_net with in coverage indicator 0, SLSS_oon
  FFS: Definition of SLSS_net, SLSS_oon
Working assumption: Priority of SLSS transmitted from in-coverage UE directly synchronized with GNSS or GNSS equivalent with sufficient reliability is the same as that of SLSS_net with in coverage indicator 1
  FFS: SLSS transmitted from in-coverage UE using GNSS or GNSS equivalent is configured by eNB
    FFS: whether the configured SLSS uses the same configuration as Rel-12 D2D SLSS or not
Working assumption: No new synchronization signal sequence is defined in V2V

## Slide 3: Proposal
For the V2V PC5 SLSS:
  SLSS ID from GNSS timing can be defined by some reserved values of the SLSS IDs:
    FFS: the detailed reserved values of the SLSS IDs
      e.g.: X1 and X2 are used for in-coverage and out-of-coverage of GNSS, where X1 and X2 are from the reserved values of the SLSS IDs
    Notes: the reserved values of the SLSS IDs can be (pre-)configured or pre-defined