## Slide 1: Way Forward on Sync Priority for OOC
3GPP TSG RAN WG1 Meeting #85 R1-165744
Nanjing, China, 23rd – 27th May 2016
Agenda Item: 6.2.2.7.1
Huawei, HiSilicon, Samsung, Panasonic, NEC, Xinwei, ITRI, ZTE

## Slide 2: Background
Working assumption: Priority of SLSS transmitted from in-coverage UE directly synchronized with GNSS or GNSS equivalent with sufficient reliability is the same as that of SLSS_net with in coverage indicator 1
Agreements: GNSS or GNSS-equivalent is at the highest priority of synchronization source for time and frequency when the vehicle UE directly receives GNSS or GNSS-equivalent with sufficient reliability and the UE does not detect any cell in any carrier.
Agreement:
  Whether eNB timing or GNSS timing is prioritized can be per carrier cell-specifically configured by the cell on which an UE camps
    The carrier that UE camps on can be different carrier other than the carrier that the priority is configured
    If the UE does not receive such a configuration, UE selects synchronization source with the same priority order as out of coverage case
  FFS: The priority order for out of coverage case

## Slide 3: Proposal
Proposal 1: Confirm the working assumption:
  Priority of SLSS transmitted from in-coverage UE directly synchronized with GNSS or GNSS equivalent with sufficient reliability is the same as that of SLSS_net with in coverage indicator 1

## Slide 4: Proposal
Proposal 2: when the UE does not detect any cell in any carrier, the UE should select its sync source according to the following priority:
  P1: GNSS or GNSS equivalent
  P2: the following SLSS has the same priority:
    SLSS_net with in-coverage indicator 1
    SLSS from in-coverage UE directly synchronized with GNSS
  The priority from the standalone UE is the lowest
  FFS : the priority of the following SLSS
    SLSS from OOC UE directly synchronized with GNSS
    SLSS indirectly synchronized with GNSS
    SLSS_net with in-coverage indicator 0