## Slide 1: Way Forward on timing offset between eNB timing and PC5 based V2V
3GPP TSG RAN WG1 Meeting #85 R1-165745
Nanjing, China, 23rd – 27th May 2016
Agenda Item: 6.2.2.7.2
Huawei, HiSilicon, Qualcomm, Intel, ZTE , Xinwei

## Slide 2: Background
We have discussed the following issues in RAN1#84b meeting:
  Proposal:
    PC5 TTI index/subframe number and frame number are derived from the UTC timing at least when GNSS is the direct synchronization reference for PC5 based V2V transmission
      FFS: how to derive the TTI index/subframe number and frame number
  Continue discussion till RAN1#85
  PC5 TTI index/subframe number and frame number can be derived from GNSS/eNB’s timing according to the configured sync source type

## Slide 3: Proposal
eNB indicates the timing offset between its timing and PC5-based V2V timing:
  FFS: granularity of the timing offset