## Slide 1: Applicability of TR38.900 channel models
Huawei, HiSilicon
3GPP TSG RAN WG1 Meeting #85 R1-165757
Nanjing, China 23rd - 27th May 2016
Agenda item 7.2.4

## Slide 2: Background
The channel model report TR38.900 has been designed to achieve the objectives of the corresponding Study Item.
Additionally, a number of requirements were agreed in Malta and added to the TR in Ljubljana.
Due to the time schedule of the SI, some of the requirements are not fullfilled.
This contribution proposes a text clarifying the applicability of the model.

## Slide 3: Proposal
The following text should be added into the TR:
  The channel model is applicable for link and system level simulations in the following conditions
    Frequency range 6 – 100 GHz (except RMa up to 7 GHz)
    Supported scenarios: urban microcell open square, urban microcell street canyon, urban macrocell, indoor office, rural macrocell.
    Supported bandwidth up to [TBD] GHz.
    Mobility support: local mobility only, parameter drifting for up to 5 meters distance of UE movement.
    Large array support is limited to far field assumption (no spherical wave) and stationary channel over the size of the array. Laplacian angular spread for large array may be questioned. The number or rays per cluster may be too low for large array.
    V2V and D2D are not supported.
    Backhaul is not supported.