## Slide 1
3GPP TSG-RAN1 Meeting #85 R1-165852
Nanjing, P.R. China, 23rd- 27th May 2016
Way Forward on Evaluation Assumptions for FeCoMP
ZTE, ZTE Microelectronics, Intel, Ericsson, Nokia, ASB, Huawei, HiSilicon, LGE, Samsung, CATT, ASTRI, Xinwei, KT Corporation

## Slide 2
Parameters | Scenario A | Scenario B | Scenario C (Co-channel ) Scenario D (Non co-channel )
Type | Indoor Hotspot | Urban Micro | Co-channel and Non co-channel urban macro with small cells
Layout | Single layer Indoor TP: Number of TPs: N=8, N=12 (optional) per 120m x 50m | Single layer Macro layer: Hex. Grid [Number of tiers: to be reported] | Two layers Macro layer: Hex. Grid Small cell layer: Random drop N TPs in the small cell cluster N = 4 TPs, N = 10 TPs [Number of tiers: to be reported]
ISD | 20m, 30m depending on the number of small cell TPs | 200m | Macro layer: 500m Small cell layer: Random
Minimum distances | According to TR 36.872 | According to TR 36.897 | According to TR 36.872
Carrier frequency | 3.5GHz | 2GHz | Macro layer: 2GHz Small cell layer: 2.0GHz (co-channel) 3.5GHz (non co-channel)
Coordination cluster size for ideal backhaul | All sites | 3 macro sites, 7 macro sites is optional, other coordination cluster size are not precluded | 3 macro sites with 3*3*N small cell TPs 1 macro sites with 1*3*N small cell TPs 7 macro sites with 7*3*N small cell TPs is optional, other coordination cluster size are not precluded

## Slide 3
System Bandwidth | 10MHz (50RBs) |  |  | 
Channel model | Indoor Hotspot (see TR 36.872) | Macro: 3D UMi (see TR 36.897) | Macro layer: 3D UMa Small cell layer: 3D UMi (see TR 36.897) | 
TP antenna configuration (M,N,P) | ULA with M=1, N=1, 2 or 4 (optional), P = 2 | Macro cell layer TP: (8,4,2), (8,8,2) optional, (8,1,2) optional Maximum number of TXRUs = 16 Small cell layer TP: M=1, N=1, 2 or 4 (optional), P = 2 |  | 
TP Tx power | 24dBm | 41dBm |  | Macro layer: 46dBm Small cell layer: 30dBm
TP antenna pattern | 2D omni with 5dBi gain (According to TR 36.872) | 3D directional with 8dBi gain (According to TR 36.873) |  | Macro layer: 3D directional with 8dBi gain (According to TR 36.873) Small cell layer: 3D directional with 5dBi gain, θetilt=90 deg, HPBWv= 40 degrees (According to TR 36.819)
TP antenna height | 6m | 10m |  | 25m for macro cells, 10m for small cells
Small cell TP dropping | According to TP layout | According to TP layout |  | According to TR 36.872
UE antenna height/UE dropping | 1.5m, uniform | According to TR 36.873 |  | According to TR 36.873
Association of UE to TP | Association method (including CRE) should be reported |  |  | 
Maximum CoMP measurement set size | Baseline 3TPs, other values are not precluded and if used should be reported |  |  | 

## Slide 4
UE antenna gain | According to TR 36.873
UE receiver noise figure | 9 dB
Traffic model | Non full buffer FTP traffic model 1, S = 0.5Mbytes
Traffic load (Resource utilization) | <5%, 20%, 40%, 70%, Optional 80% (S=0.1Mbytes)
UE receiver | MMSE-IRC and CWIC as the baseline receiver (other advanced SU-MIMO receivers are not precluded)
UE antenna | 2Rx, 4Rx (only for JT), 00/900 polarization slants, 0.5 wavelength spacing
Feedback assumption | PUSCH 3-2
Transmission mode | TM10 based
Number of CSI-RS antenna ports | Non coherent JT: 2 or more ports per NZP CSI-RS resource CS/CB for FD-MIMO: 2 or more ports per NZP CSI-RS resource (total number of CSI-RS ports up to 16)
Channel estimation | Realistic
CRS interference modelling | CRS modelling should be provided
Handover margin | 3dB
Backhaul link delay | 0ms, 2ms (optional), 5ms, 50ms
Baseline scheme | Option 1: DPS/DPB for JT, Single point for CS/CB Option 2: Rel-11 CoMP and non-CoMP Rel-13 FD-MIMO Option 3: Provided by each company