## Slide 1: WF on UL 256QAM TBS table
Huawei, HiSilicon, CMCC, CATR, China Unicom, China Telecom, ZTE, Deutsche Telekom, Sprint, AT&T,…
R1-165880
3GPP TSG RAN WG1 Meeting #85
Nanjing, China, May 23–27, 2016
Agenda item 6.2.8

## Slide 2: Background
Agreement
  Reference number of REs available in PUSCH for UL 256QAM TBS design is 144 REs/PRB
  The maximum coding rate for PUSCH with 256QAM should not exceed 0.931
  FFS whether or not to introduce new TBS index(es) for PUSCH with 256QAM
    Companies are encouraged to submit evaluations to RAN1#85
If Rel-12 TBS table is reused to support UL 256QAM, uplink coding rate is reduced by 8% than downlink.
  The uplink spectral efficiency is 8% lower than potential spectral efficiency.

## Slide 3: Proposals
Introduce new TBS index(es) for PUSCH with 256QAM to increase coding rate