## Slide 1
3GPP TSG RAN WG1 Meeting #85 R1-165920
Nanjing, China, 23rd - 27th May 2016
Agenda item: 6.2.3.2.2
WF on Additional Hybrid CSI Mechanism
NTT DOCOMO, LG Electronics, NEC, Qualcomm, Samsung

## Slide 2: Background
Working assumption:
Mechanism 1: Hybrid CSI is realized by with one CSI process, support at least CLASS A for the 1st eMIMO-Type and CLASS B with K=1 CSI-RS resource for the 2nd eMIMO-Type
  i1 is reported while CQI and i2 are not reported for the 1st eMIMO-Type (CLASS A)
    FFS: whether RI is reported for CLASS A
  CQI/PMI/RI are reported for the 2nd eMIMO-Type (CLASS B K=1)
At least one more mechanism is supported, to be discussed in RAN1#86

## Slide 3: Proposal
Confirm working assumption for mechanism 1 as an agreement
Agree on mechanism 2: for hybrid CSI with one CSI process, support CLASS B with K≥1 CSI-RS resources for the 1st eMIMO-Type and CLASS B with K=1 CSI-RS resources for the 2nd eMIMO-Type
  For the 1st eMIMO-Type, depending on the value of K
    K=1: CQI, RI and i1 are reported
    K>1: two options
      Option 1: CRI is reported
      Option 2: PMI/RI for each CSI-RS resource are reported
  For the 2nd eMIMO-Type
    CQI/PMI/RI are reported