## Slide 1: WF on ED Threshold for UL LBT
Ericsson, Huawei, HiSilicon
3GPP TSG RAN WG1 #85 R1-165962
Nanjing, China
23rd – 27th May 2016
Agenda item: 6.2.1.5
Document for decision

## Slide 2: Background
Coexistence of LAA with Wi-Fi in 3GPP scenarios based on LAA with ED threshold of -72 dBm for both DL and UL LBT are presented in e.g. R1-165158 where no coexistence issue with the neighboring Wi-Fi network is observed.
Coexistence of LAA with Wi-Fi in scenarios based on LAA with ED threshold of -72 dBm with an RSSI profile similar to reported field measurements R1-162982 are presented here:

## Slide 3: Background
Simulation assumptions:
8 APs per operator
25 users per operator
50/50 DL and UL split
LAA:
  Self-carrier scheduling
  UL LBT: CCA of 25us
  ED THS=-72 dBm (DL &UL)
Other assumptions as in

## Slide 4: Background
Observation: Wi-Fi network can coexist well with an LAA network
User DL Throughput
User UL Throughput

## Slide 5: Proposal
Align the requirement on the energy detection threshold for UL transmission with the corresponding Rel-13 LAA requirements for PDSCH transmission.