## Slide 1: Way forward on calibration assumptions for NR waveform
Huawei, HiSilicon, NTT DOCOMO, Nokia
3GPP TSG RAN WG1 Meeting #85 R1-165989
Nanjing, China, 23th – 27th May2016
Agenda Item: 7.1.2

## Slide 2: Background
Assumptions | Value
Carrier frequency | 4GHz
Duplex | FDD/TDD
System Bandwidth | 10 MHz
TTI length | 1 ms as baseline, other TTI length is FFS (e.g. short TTI )
Subcarrier spacing | Single numerology case: 15KHz as baseline, Mixed numerology case: one is 15KHz, and the other subcarrier spacing should be selected by companies from the agreed numerologies.
Guard time interval | 4.7us (interval of LTE normal CP) as baseline, other interval is FFS
FFT size | e.g. 1024 for 15KHz subcarrier spacing
Data transmission bandwidth | Single numerology case: 4 and/or 1 PRBs for the bandwidth of target UE in case 1b Mixed numerology case: At least two candidate BWs for target UE. At least two candidate BWs for interfering subband At least two numerologies. The values are FFS
Guard tone number | [0~12] subcarriers for the mixed numerology case
Antenna configuration | 1T1R or 2T2R or 4T4R, other is not precluded
MIMO mode | Follow the agreements of email discussion [84b-14]
Rank per UE | Fixed rank
MCS | Fixed. 16QAM: 1/2 or 2/3; 64QAM: 1/2 or 3/4; 256 QAM: 1/2 or 3/4
Control Overhead | Zero
Channel estimation * | Ideal
Channel Model ** | Follow the agreements of email discussion [84b-14]
Agreed Parameters for case 1a/1b and case 2
NOTE: *Non-ideal effects to be considered in a second stage (e.g., channel estimation, frequency offset, details are FFS)

## Slide 3
Assumptions | Value
Carrier frequency | 4GHz
Duplex | FDD/TDD
System Bandwidth | 10 MHz
TTI length | 1 ms
Subcarrier spacing | Single numerology case: 15KHz as baseline, Mixed numerology case: target UE is 15KHz, and interferer is 30 KHz
Guard time interval | 6.7% overheads
FFT size | 1024 for 15KHz
Data transmission bandwidth | case 1a: 9 MHz; case 1b: 720KHz,
UE bandwidth (data transmission bandwidth plus guard tone bandwidth of the desired UE) | case 2: 720KHz per UE
Bandwidth of guard tones between neighboring UEs | case 2: 60 KHz
Antenna configuration | 1T1R
MCS | 64QAM: 1/2
Control Overhead | Zero
Channel estimation | Ideal
Channel Model | TDL-C for DS 300ns, Mobility: 3km/h
Proposal
The following values are used for calibration purpose in case 1a, 1b, 2:

## Slide 4: Proposal
Use an email discussion to collect the calibration results for all agreed simulation cases before RAN1#86 meeting.
  OFDM/DFT-S-OFDM with CP as baseline for performance reference. (LMMSE receiver assumed)
  At least BLER vs SNR should be reported for calibration
  Note: This calibration is not for down-select purpose.
  Note: The selection of the parameters on page 3 is only for calibration purpose