## Slide 1: Proposal for email discussion on evaluation assumptions for high speed train scenario: Macro + relay around 30GHz
Mitsubishi Electric, ETRI
3GPP TSG RAN WG1 Meeting #85 R1-166001 Nanjing, China, 23th - 27th May 2016
Agenda item: 7.1.2

## Slide 2
Layout | Refer to R1-165484
Inter-RRH distance | Refer to R1-165484
Carrier frequency | Around 30GHz
Aggregated system bandwidth | Up to 1GHz (DL+UL)
Simulation bandwidth | [100] MHz
Channel model | 5GCM TDL, CDL-D/E Note: Other models can be considered.
RRH and Relay power | RRH Tx power: [30dBm] Relay Tx power： [27dBm] System bandwidth: [100MHz or more]
RRH antenna elements | Up to 256 Tx /Rx antenna elements
RRH antenna architecture | FFS, Starting point is the multi antenna architecture agreed for the NR MIMO study
RRH antenna height | 2.5m
RRH antenna element gain + connection loss | FFS
RRH receiver noise figure | FFS
Relay antenna elements | Up to 256 Tx /Rx antenna elements
Relay antenna architecture | FFS, Starting point is the multi antenna architecture agreed for the NR MIMO study
Relay antenna height | FFS
Relay antenna gain | FFS
Relay receiver noise figure | FFS
Channel estimation | Realistic
Maximum speed | 500 km/hr
Proposal : Email discussion for FFS, square bracketed parameters and other link level simulation related parameters