## Slide 1
3GPP TSG RAN WG1 Meeting #85 R1-166020
Nanjing, China, 23th - 27th May 2016
Agenda item: 7.1.2
Way forward on High Speed Link Level evaluation
Cohere, AT&T, CMCC, Deutsche Telekom, InterDigital, National Taiwan University, Orange, Spreadtrum, Telefonica, Telstra

## Slide 2: Motivation
It has been agreed that link level evaluation is needed for the high speed train scenario (R1-165576)
Highway and V2X scenarios also require high speed to be studied
Waveform candidates should be evaluated in one or more high speed scenarios

## Slide 3: Proposal
NR waveform evaluation should include performance assessment in high speed scenarios

## Slide 4
Assumptions | Value
Carrier frequency | 4GHz
Duplex | FDD/TDD
System Bandwidth | 10 MHz
TTI length | 1 ms
Subcarrier spacing | Single numerology case. Companies should report the selected value
Guard time interval | 4.7us (interval of LTE normal CP) as baseline, other interval is not precluded
FFT size | e.g. 1024 for 15KHz subcarrier spacing
Data transmission bandwidth | Single numerology case: 50, 4 PRBs
Antenna configuration | 1T1R, 2T2R
MIMO mode | Open loop [Companies should describe precoding scheme]
Rank per UE | Fixed rank
MCS | Fixed. QPSK: 1/2, 16QAM: 1/2
Performance metric | User Spectral efficiency (bps/Hz)*
Control Overhead | Zero
Channel estimation | Realistic (describe pilot arrangement)
Channel Model | TDL-C, ITU Rural Macro
Mobility | 500 Km/h
Proposal on High Speed LLS evaluation
  * Computed according to R1-163897