## Slide 1
3GPP TSG-RAN1 Meeting #85 R1-166026
Nanjing, P.R. China, 23rd- 27th May 2016
WF on the antenna model for outdoor TRP
Intel, NTT DOCOMO, ZTE, Samsung, Xinwei, CATT, Ericsson, Nokia, ASB, Huawei
Agenda item: 7.1.2

## Slide 2: Proposal
The possible options for outdoor micro cell TRP antenna element model and placement:
  Option 1: Omni in horizontal, directional in vertical ([5]dBi gain, HPBW [400], vertical tilt 900)
    Dropping in the center of the hotspot area
  Option 2: Directional in horizontal, directional in vertical ({8dBi gain, HPBW = 650}; {4dBi gain, HPBW = 1300})
    One-sector deployment
      Dropping of TRP and TRP antenna orientation according to TR 36.897 (non co-channel hetnet deployment)
    Three-sector deployment
      Dropping of TRP in the center of the hotspot area
      Option A: Azimuth orientation of TRP antenna is random
      Option B: Azimuth orientation of TRP is according to macro TRP deployment
  RAN1 to choose from the above options in RAN1#86 for the above 6GHz and below 6GHz and other options are not precluded