## Slide 1: WF on further evaluation assumptions for NR waveform 30GHz and beyond
Nokia, Alcatel-Lucent Shanghai Bell, Intel, Samsung, Huawei, HiSilicon,Qualcomm
3GPP TSG RAN WG1 Meeting #85 R1-166028
Nanjing, China, 23rd – 27th May 2016
Agenda Item: 7.1.3.1

## Slide 2: Proposal
Assumptions , | Value
Carrier frequency | 30 GHz & 70 GHz
Duplexing | TDD
Simulation case | Case 1a /1b
System bandwidth | 30 GHz: 80 MHz or above, 70 GHz: 640MHz or above, other values are not precluded.
Data bandwidth | DL: 90% of system bandwidth UL: 4PRBs (48 subcarriers) or 90% of system bandwidth
Numerology | FFS: Depend on numerology progress (subframe duration, guard time interval, # of symbols per subframe, subcarrier spacing if needed)
UE antenna model | (M,N,P,Mg,Ng) = (2, 4, 2, 1, 1) or (2, 2, 2, 1, 1)
TRP antenna model | (M,N,P,Mg,Ng) = (8, 8, 2, 1, 1) for 30GHz, (8,16,2,1,1) for 70GHz. Option 1: a single TXRU is mapped per panel per polarization. DFT vector is used to map TXRU to antenna elements. Per antenna element pattern is in [1]
Phase noise model | Follow the agreement in R1-165685
Channel coding | LTE Turbo code, other coding scheme is not precluded
Rank per UE | Rank 1 or 2
MCS | BPSK(pi/2) 1/2, QPSK(pi/4) 1/3, QPSK: 1/2, 16QAM: 1/2 or 2/3; 64QAM: 1/2 or 3/4; 256QAM ¾
Channel estimation | Ideal, Realistic* (Pilot pattern to be given in the case of real channel estimation)
Channel model | CDL-{A,B,C} in TR 38.900 with {50, 300***, 800} ns DS, with 15 degrees AoD spread for TRP, 45 degrees AoA for UE 3km/h, 30km/h (optional) Beam forming scheme used for spatial filtering needs to be reported
Table 1 Parameters for high frequency bands
NOTE: * For realistic channel estimation, the current LTE DL/UL DMRS is recommended. Pilot overheads should be considered into the calculation of user spectrum efficiency.
* * CDLs are scenario agnostic.
*** Recommended for calibration
[1] TR36.873_v210 table 7.1.1 Antennal element vertical & horizontal radiation pattern