## Slide 1: Channel Coding for NR
NTT DOCOMO, INC.
3GPP TSG RAN WG1 Meeting #86
Gothenburg, Sweden 22nd - 26th August 2016
Agenda Item: 8.1.4.1
R1-167624

## Slide 2: Requirements
Good performance for variable data size
  From small data to large data
  With wide variation of coding rate
  Support of IR as a baseline
Low decoding latency/complexity
  Low complexity may lead to low energy consumption
Support of ultra high reliability
  No error floor preferred for URLLC, if retransmission is not allowed
Combination of requirements needs to be considered

## Slide 3: Channel Code Candidates
Multiple codes may be needed for NR to support full combinations of requirements
Large data
performance
Small data
performance
High reliability
Low latency/complexity
LDPC/Turbo
Conv. code
Polar?
Conv. code with LIST decoding
LDPC (Turbo) with LIST decoding?
Note: Other coding scheme (if feasible) needs to be checked

## Slide 4: Proposed Primary Study Points
The best code for large data with low latency/complexity
  LDPC vs. Polar vs. Turbo (as reference)
The best code for small data with high reliability
  Polar vs. Conv. code with LIST decoding
High reliability
Low latency/complexity
Relevant for eMBB
Relevant for eMBB
and URLLC
(can be used also for mMTC)
Large data
performance
Small data
performance

## Slide 5: Example Combinations
LDPC (or Turbo) + Polar codes
  LDPC (or Turbo) for large data with low latency/complexity
  Polar for small data and/or high reliability
LDPC (or Turbo) + Conv. codes
  LDPC (or Turbo) for large data with low latency/complexity
    With LIST decoding for high reliability???
  Conv. code for small packet with low latency/complexity
    With LIST decoding for high reliability
Polar code only (if feasible…)
Two schemes at maximum should be supported in NR Phase I

## Slide 6
Preliminary Evaluation of Polar Code/TBCC

## Slide 7: Performance

## Slide 8: Simulation Parameters
In this contribution, we follows the agreed simulation assumption for URLCC and mMTC
Parameters | Values or assumptions |  |  | 
Channel* | AWGN |  |  | 
Modulation | QPSK, 16QAM |  |  | 
Coding Scheme | Convolutional codes | LDPC | Polar | Turbo
Code rate | 1/12, 1/6, 1/3 |  |  | 
Decoding algorithm | List-X Viterbi | min-sum | List-Y | Max-log-MAP
Info. block length (bits w/o CRC) | 20, 40, 200, 600, 1000 |  |  | 

## Slide 9: Convolutional Code
Tail-biting convolutional code employing generator polynomial of (133, 171, 165) is used (same as LTE)
Rate matching also follows LTE
16 bits CRC (assumed to be ideally detected) is used for selecting the code words
  Therefore, CRC insertion loss considered to calculate Eb/N0
The LVA selects the best-L surviving paths per STATE
List size, L, is parameterized to obtain the performance for different complexity

## Slide 10: Polar Code
Quasi-uniform puncturing is used to fit the code word size
  e.g., 60 bits code word size is generated by puncturing 4 bits from 64bits
16 bits CRC (assumed to be ideally detected) is used for selecting the code words
  Therefore, CRC insertion loss considered to calculate Eb/N0
List size, L, is parameterized to obtain the performance for different complexity

## Slide 11: k=20bits, n=60bits (R=1/3)
Eb/N0 (dB)
BLER
L=1
L=2
L=8
L=32
Polar code
TBCC
Comparison in same number of list size (L: List size)
 |  | Polar | TBCC | TBCC/Polar
L | 1 | 576 | 19263 | 33.4
 | 2 | 1408 | 29567 | 21.0
 | 8 | 7680 | 116991 | 15.2
 | 32 | 38912 | 589567 | 15.2
Complexity comparison
(detail is described in slide #17,#18)

## Slide 12: k=40bits, n=120bits (R=1/3)
Eb/N0 (dB)
BLER
L=1
L=2
L=8
L=32
Polar code
TBCC
 |  | Polar | TBCC | TBCC/Polar
L | 1 | 1280 | 38463 | 30.0
 | 2 | 3072 | 59007 | 19.2
 | 8 | 16384 | 233471 | 14.2
 | 32 | 81920 | 1177087 | 14.4
Comparison in same number of list size (L: List size)
Complexity comparison
(detail is described in slide #17,#18)

## Slide 13: k=200bits, n=600bits (R=1/3)
Eb/N0 (dB)
BLER
L=1
L=2
L=8
L=32
Polar code
TBCC
 |  | Polar | TBCC | TBCC/Polar
L | 1 | 13312 | 115903 | 8.7
 | 2 | 30720 | 218367 | 7.1
 | 8 | 155648 | 1089151 | 7.0
 | 32 | 753664 | 5801087 | 7.7
Comparison in same number of list size (L: List size)
Complexity comparison
(detail is described in slide #17,#18)

## Slide 14: k=600bits, n=1200bits (R=1/3)
Eb/N0 (dB)
BLER
L=1
L=2
L=8
L=32
Polar code
TBCC
 |  | Polar | TBCC | TBCC/Polar
L | 1 | 28672 | 320703 | 11.2
 | 2 | 65536 | 627967 | 9.6
 | 8 | 327680 | 3239551 | 9.9
 | 32 | 1572864 | 17372287 | 11.0
Comparison in same number of list size (L: List size)
Complexity comparison
(detail is described in slide #17,#18)

## Slide 15: k=1000bits, n=3000bits (R=1/3)
Eb/N0 (dB)
BLER
L=1
L=2
L=8
L=32
Polar code
TBCC
 |  | Polar | TBCC | TBCC/Polar
L | 1 | 61440 | 521023 | 8.5
 | 2 | 139264 | 1033087 | 7.4
 | 8 | 688128 | 5385471 | 7.8
 | 32 | 3276800 | 28939007 | 8.8
Comparison in same number of list size (L: List size)
Complexity comparison
(detail is described in slide #17,#18)

## Slide 16: Complexity

## Slide 17: Polar Code (SCLD)
 | Addition (Subtraction) | Comparison
f operation |  | L(N/2)log2N
g operation | L(N/2)log2N | 
Path Metric calculation | LN | 
Sort |  | 2LN(log2(2L))
Total number of operation | LN{(1/2)log2N+1} | LN{(1/2)log2N+2log2(2L)}
N: Total number of coded bits (including puncturing)
L: List size
Cost of addition and comparison is assumed to be equal

## Slide 18: TBCC
 |  | Addition (Subtraction) | Comparison
Initial state estimation | Branch metric calculation | 2S(1/R-1)kh | 
 | Path metric calculation | 2Skh | Skh
Sequence estimation | Branch metric calculation | 2S(1/R-1)k | 
 | Path metric calculation | 2LSk | 
 | Sort |  | 2LSk(log2(2L))
 | Find optimum path |  | LS-1
Total number of operation |  | 2S{(1/R-1) (kh+k)+kh+Lk} | Skh+LS-1 +2SLk(log2(2L)
k: Total number of information bits, kh: Total number of head bits
S: Number of state, L: List size, R: Coding rate before rate matching (=1/3)
Cost of addition and comparison is assumed to be equal