## Slide 1: Proposals on collision handling for SRS switching
SoftBank
3GPP TSG RAN WG1 Meeting #86 R1-167757
Gothenburg, Sweden 22nd – 26th August 2016

## Slide 2: Background(1)
RAN1 agreed the following options for collision handling:
Agreement: To handle collision due to SRS carrier-based switching Define priority/dropping rules by taking into account the factors including periodic/aperiodic SRS type, channel/UCI type, and PCell/SCell type Rel-13 collision handling rules between SRS and other UL transmissions as baseline, taking into account switching time based on input from RAN4 Details FFS FFS shortened PUSCH format and possible mechanisms to mitigate the effect of puncturing (e.g. power control, different beta value for UCI). FFS approaches to help avoid collision, e.g., Introduction of different HARQ timing (e.g. by introduction of HARQ reference subframes) Introduction of flexible A-SRS transmission timing Group DCI for A-SRS triggering

## Slide 3: Background(2)
RAN4 agreed multiple values for RF switching time (LS response: R1-166084) because it depends on CA scenario and UE implementation.
  RF switching time: [<100] us, [100] us, 200 us, 300 us, 500 us, 900 us
It implies that the collision handling is dependent on the switching time of the UE.
  For example, if the UE can switch the carrier with very short interruption time (e.g. within one symbol), there is no collision with UCI on the UL subframe because the switching can be done in the SRS symbols in the special subframe.

## Slide 4: Considerations of collision handling
Regarding FFS options, it seems to need additional study and significant impacts on RAN1 specifications.
In addition, RAN1 should consider that RAN2 will start a discussion with very limited TU (0.5 TU per meeting; 1TU in total) regarding higher layer signaling from the next meeting.

## Slide 5: Proposals on collision handling
Proposals:
  RAN1 should address the priority/dropping rules as a baseline solution for the collision handling.
  If RAN1 cannot agree with a proposed option in principle in RAN1#86, the option should not be considered in Rel-14.

## Slide 6: Considerations on switching time
The UE should report the switching time information for an appropriate eNB scheduling.
From the eNB point of views, it seems more important to distinguish whether SRS switching can be performed without PUCCH/PUSCH interruption or not.
  Because it relates to the necessity of collision handling.
Precise switching time information may be used for optimization for each of solutions, but it is not essential.

## Slide 7: Proposals on switching time
Proposals:
  Before entering the discussion, RAN1 should decide an upper limit value of time whether to indicate support of the SRS switching.
  The UE should indicate capability information indicating;
    (a) SRS switching is supported without interruption of other CC or
    (b) SRS switching is supported with interruption of other CC.