## Slide 1
3GPP TSG RAN WG1 Meeting #86 R1-167960 Gothenburg, Sweden, 22nd - 26th Aug 2016
Agenda item: 8.1.5
WF on QCL assumptions in NR
Huawei, HiSilicon, China Telecom, DoCoMo

## Slide 2: Background
The following agreements have been reached at RAN1#85:
  Study necessity of QCL and measurement assumptions for antenna ports in NR
  It should be possible as one option to assume QCL between ports of two different panels of the same transmission points

## Slide 3: Proposal
For the QCL assumptions and configurations, the following should be supported:
  By default, no QCL assumptions in NR for the following cases unless explicitly or implicitly indicated
    between synchronization signals and CSI-RS
    between synchronization signals and DM-RS
  By default, no QCL assumptions for antenna ports transmitted in different time occasions (e.g. different subframes or TTIs) in NR unless explicitly or implicitly indicated
  With explicit or implicit indications, NR should
    support multiple QCL configurations
    support flexible QCL configurations at least for the following cases:
      Among CSI-RS ports
      Among DMRS ports
      Between different types of antenna ports
      FFS: among other types of RS ports in addition to CSI-RS and DMRS