## Slide 1: WF on Scalable Numerology Symbol Boundary Alignment
Qualcomm Inc., ZTE, [OPPO, Interdigital, ETRI, NEC, OPPO , Panasonic, DoCoMo, Deutsch Telecom]
3GPP TSG RAN WG1 #86 R1-167969
Gothernburg, Sweden
22th – 26th Aug 2016
Agenda item:8.1.3
Document for decision

## Slide 2: Proposal
When different numerologies are multiplexed:
  With the same CP overhead, OFDM symbol boundaries are aligned across scaled numerologies
For any scaled numerology Fj = Fi*2M, in the case where numerology (of SCS = Fi) contains N symbols per ms and numerology (of SCS = Fj) contains N*2M symbols per ms
  Each symbol length (including CP) of numerology (of SCS = Fi) equals the sum of the corresponding length (including CP) of 2M symbols of scaled numerology (of SCS = Fj)

## Slide 3: Illustrations
Symbol alignment within a given reference numerology
Reference numerology SCS = 15kHz, N=7, NCP
Symbol is aligned at the boundary
15 kHz
30 kHz
60 kHz
7.5 kHz
0.5 ms
3.75 kHz