## Slide 1: WF on Flexibility of Channel Coding Techniques
Ericsson, Nokia, ASB, LGE
R1-167993
3GPP TSG RAN WG1 Meeting #86
Gothenburg, Sweden, 22-26 August 2016
Agenda item 8.1.4.1

## Slide 2: Proposal
  Channel coding techniques for NR should support code size and code rate flexibility
    Info block size K flexibility:
      At least support D1-bit granularity at lower end of K; D2-bit granularity at higher end of K, D1<=D2, value of D1 and D2 are FFS
      A different granularity for mid-range K can be included
    Codeword size flexibility:
      Basic code design with rate matching supports 1-bit granularity
    Note: not all use cases are required to utilize the full flexibility provided by the channel coding technique
  Shortening and rate matching (i.e., puncturing and/or repetition) are utilized to provide flexibility in addition to the basic code design