## Slide 1: WF on Channel Coding Selection for NR
Huawei, HiSilicon, CMCC, CUCC, Deutsche Telekom, Orange, Telecom Italia, Vodafone, China Unicom, Spreadtrum
3GPP TSG RAN WG1 #86 R1-168040
Gothenburg, Sweden, Aug 22 - 26, 2016
Agenda item: 8.1.4.1

## Slide 2: Background
Agreements in RAN#84b
  Candidates for 5G new RAT data transmission are identified as the following
    LDPC code
    Polar code
    Convolutional code (LTE and/or enhanced convolutional coding)
    Turbo code (LTE and/or enhanced turbo coding)
mMTC | URLLC
Convolutional codes | Convolutional codes
LDPC | LDPC
Polar | Polar
Turbo | Turbo
Agreements in RAN#85 on code comparison
  Observations on AWGN performance for small information block and low code rate (from 1/12 to 1/3)
  WF on channel coding simulation data sharing
  WF on further study of complexity of channel code

## Slide 3: Observations
RAN1#85 Observation: For large information block sizes, all candidate channel coding schemes show comparable link performance
Polar codes are better than convolutional codes, turbo codes, and LDPC codes for small block lengths (from 80 to 1000 bits)
  ~2 or more dB better than convolutional codes [R1-167216]
  0.5-1dB better than turbo code [R1-167212]
  Up to 1dB better than LDPC codes [R1-167212]
    NOTE: LDPC codes do not support 1-bit granularity
Polar and LDPC are both feasible to implement at high data rates[R1-167213]
Polar code meets the URLLC latency requirement [R1-167213]

## Slide 4: Way Forward
  Polar code is a candidate channel coding technique for NR for eMBB, URLLC, mMTC