## Slide 1: WF on scenarios and evaluation assumptions for flexible duplex
LG Electronics, Huawei, HiSilicon
3GPP TSG RAN1 #86
Gothenburg, Sweden, Aug 22 - 26, 2016
Agenda Item: 8.1.7
R1-168053

## Slide 2: Proposal
For studying and evaluating of flexible duplex operation, at least consider dense urban, urban macro, and indoor hotspot scenarios.

## Slide 3
Agree the following evaluation assumptions for flexible duplex:
Parameters | Dense urban | Urban macro | Indoor hotspot
Layout | Two layer: Macro layer: Hex. Grid Micro layer: Random drop (All micro BSs are outdoor) 3 micro BSs per macro BS | Single layer: Macro layer: Hex. Grid | Single layer: Indoor floor (12 BSs per 120m X 50m)
Inter-BS distance | Macro-to-macro: 200m Macro-to-micro: 105m [TR36.897] Micro-to-micro: 57.9m | 500m | 20m
Minimum BS-UE (2D) distance | Macro-to-UE: 35m [TR36.897] Micro-to-UE: 10m [TR36.897] | 35m [TR36.897] | 0m [TR38.900]
Minimum UE-UE (2D) distance | 3m [TR36.843] |  | 
Carrier frequency | Macro layer: 4 GHz, 30 GHz [TR38.913] Micro layer: 4 GHz, 30 GHz | 2GHz [TR38.913], 4 GHz, 30 GHz | 4 GHz, 30 GHz
 | For 30GHz: Un-paired spectrum is preferred. For 2GHz: paired spectrum is preferred. For 4GHz: both paired and un-paired spectrum can be considered. |  | 
Aggregated system bandwidth | 4GHz: Up to 200MHz (DL+UL) 30GHz: Up to1GHz (DL+UL) | 2GHz: Up to 40 MHz (DL+UL) 4GHz: Up to 200 MHz (DL+UL) 30GHz: Up to 1GHz (DL+UL) | 4GHz: Up to 200MHz (DL+UL) 30GHz: Up to 1GHz (DL+UL)
Simulation bandwidth | 20MHz per CC below 6GHz and 80 MHz per CC above 6GHz Note: For FDD, simulation BW is split equally between UL and DL Note: UE TX power scaling will impact final results |  | 
Proposal (marked with red)

## Slide 4
Parameters | Dense urban | Urban macro |  | Indoor hotspot
Channel model | Below 6GHz: Macro-to-UE: 3D UMa Micro-to-UE: 3D UMi Macro-to-Macro: 3D UMa (h_UE=25m) Macro-to-Micro: 3D UMa (h_UE=10m), FFS additional offset X1 dB Micro-to-Micro: 3D UMi (h_UE=10m), FFS additional offset X2 dB UE-to-UE: A.2.1.2 in TR36.843, FFS on penetration loss between UEs Above 6GHz: Macro-to-UE: 5GCM UMa Micro-to-UE: 5GCM UMi Macro-to-Macro: 5GCM UMa (h_UE=25m) Macro-to-Micro: 5GCM UMa (h_UE=10m) Micro-to-Micro: 5GCM UMi (h_UE=10m) UE-to-UE: 5GCM UMi (h_BS=1.5m ~ 22.5m), FFS on penetration loss between Ues |  |  | Below 6GHz: TRP-to-UE: ITU InH TRP-to-TRP: ITU InH (h_UE=3m) UE-to-UE: A.2.1.2 in TR36.843 Above 6GHz: TRP-to-UE: 5GCM Indoor-office TRP-to-TRP: 5GCM Indoor-office (h_UE=3m) UE-to-UE: 5GCM Indoor-office (h_BS=1.5m)
Large-scale channel parameters | FFS |  |  | 
Fast fading parameters | FFS |  |  | 
BS Tx power | Below 6GHz: 44 dBm PA scaled with simulation BW when system BW is higher than simulation BW. Otherwise, 44 dBm Above 6GHz: 33 dBm PA scaled down with simulation BW when system BW is higher than simulation BW. Otherwise, 33 dBm | Below 6GHz: 49 dBm PA scaled with simulation BW when system BW is higher than simulation BW. Otherwise, 49 dBm Above 6GHz: 43 dBm [scaled with simulation BW when system BW is higher than simulation BW. Otherwise, 43 dBm] | Below 6GHz: 24 dBm PA scaled with simulation BW when system BW is higher than simulation BW. Otherwise, 24 dBm Above 6GHz: 23 dBm [scaled with simulation BW when system BW is higher than simulation BW. Otherwise, 23 dBm] | 

## Slide 5
Parameters | Dense urban | Urban macro | Indoor hotspot
UE Tx power | 23 dBm |  | 
BS antenna configuration | Below 6GHz: Baseline: (M,N,P,Mg,Ng)=(8,8,2,1,1) (dH,dV)=(0.5,0.8)λ Above 6GHz: Baseline: (M,N,P,Mg,Ng)=(4,8,2,2,2) (dH,dV,dH,g,dV,g)=(0.5,0.5,4.0,2.0)λ | Below 6GHz: Baseline: (M,N,P,Mg,Ng)=(8,8,2,1,1) (dH,dV)=(0.5,0.8)λ Above 6GHz: Baseline: (M,N,P,Mg,Ng)=(4,8,2,2,2) (dH,dV,dH,g,dV,g)=(0.5,0.5,4.0,2.0)λ | FFS
BS antenna height | Macro: 25m Micro: 10m | 25m | 3m
BS anteena element gain + connector loss | 8 dBi | 8 dBi | 5 dBi
BS receiver noise figure | Below 6GHz: 5 dB Above 6GHz: 7 dB |  | 
UE antenna configuration | Follow the Table A.2.1-3 of TR38.802 |  | 
UE antenna height | hUT=3(nfl-1)+1.5 nfl for outdoor UEs: 1 nfl for indoor UEs: nfl~uniform(1,Nfl) where Nfl~uniform(4,8) |  | 1.5m
UE antenna gain | Follow the modeling of TR36.873 |  | 

## Slide 6
Parameters | Dense urban | Urban macro | Indoor hotspot
UE receiver noise figure | Below 6GHz: 9 dB Above 6GHz: 13 dB |  | 
Traffic model | Baseline: FTP traffic model 3 with packet size 0.1 and 0.5Mbytes Ratio of DL/UL traffic = {2:1}, {4:1} [TR36.828] |  | 
UE distribution | For FTP traffic model 3: 2/3 users randomly and uniformly dropped within the clusters, 1/3 users randomly and uniformly dropped throughout the macro geographical area, and 60 users per macro geographical area 80% indoor (3km/h) and 20% outdoor (30km/h) | For FTP traffic model 3: 10 users per macro TRP 80% indoor (3km/h) and 20% outdoor (30km/h) | For FTP traffic model 3: 10 users per TRP 100% indoor (3km/h)
UE receiver | MMSE-IRC as the baseline receiver |  | 
BS receiver | MMSE-IRC as the baseline receiver |  | 
Feedback assumption | Realistic |  | 
Channel estimation | Realistic |  |