## Slide 1: WF on new P2x transmission mode
Ericsson
3GPP TSG RAN WG1 Meeting #86 R1-168083
22nd – 26th August, 2016 Gothenburg, Sweden
Agenda item: 7.2.3.2

## Slide 2: Background
RAN plenary indicated in WID RP-161298:
  3) To specify enhancements for support of V2P service:
  a) Random resource selection for P-UEs potentially on the PC5 resource pool shared with V-UE transmissions, with additional study on sensing operation during a limited time for P-UEs [RAN1, RAN2]
  b) Authorization for pedestrian UEs, if necessary [RAN3, RAN2 if needed]

## Slide 3: Background
Clearly UEs performing random selection may create additional interference to UEs performing sensing and it is useful to let the NW be able to control such interference by configuration.
It is necessary to have a transmission mode for P2X with optimizations for reduced energy consumption.
  As in mode 2, UEs using this TM should be able to transmit over PC5 even when in IDLE in their cell to avoid the energy-costly process of maintaining the connection to the eNB.
Regarding reception, we believe that for pedestrians delay constraints can be relaxed (as compared to V2V). Additionally, monitoring the V2X pools might quickly drain the battery.
  Therefore, it does not seem urgent to require sidelink reception capabilities for pedestrians, i.e., pedestrians can monitor the Uu multicast channel to receive vehicles presence warnings

## Slide 4: Proposals
A new “V2X Transmission Mode 3” is introduced for random resource selection.
V2X Transmission Mode 3 is only allowed in a dedicated “Transmission Mode 3” pool.
  The TM3 pool may overlap with TM1 and TM2 pools according to NW (pre)configuration.
Use mode-3 as a resource selection mode that is suitable for handheld devices
  No sidelink reception capabilities required for mode-3
  IDLE operation supported
  Limited OOC operation if device does not have SS/PDSCH detection capability.