## Slide 1
Way Forward on SLS assumptions for autonomous/grant-free/contention-based MA
LG Electronics, ZTE, ZTE Microelectronics
R1-168115
3GPP TSG RAN WG1 #86
Gothenburg, Sweden, 22nd – 26th August 2016
Agenda item 8.1.2.2

## Slide 2: Proposal
Traffic model for autonomous/grant-free/contention-based MA is as follows :
Attributes | Value or assumptions
Data packet arrival rate per UE | Poisson arrival with arrival rate, λ
Physical layer target packet size | Fix 40 Bytes
Simulation Bandwidth | Companies report the simulation bandwidth
packet drop rate | 0.01

## Slide 3: Proposal
One of performance metrics of SLS for autonomous/grant-free/contention-based MA
  packet drop rate vs. packet arrival rate curve
  Note: packet arrival rate reflects system loading, e.g. number of arrived packets per cell per sec.