## Slide 1: WF on Battery Models
Sony, u-blox, Sierra Wireless
R1-168128
3GPP TSG RAN WG1 #86
Gothenburg, Sweden, 22nd -26th August, 2016
Agenda item 8.1.7

## Slide 2: Background
RAN1#85 discussed the need for a corresponding evaluation methodology and UE energy consumption model for assessing the merits of different technical solutions. Companies are invited to propose a simple UE energy modelling approach for NR mMTC radio access energy efficiency analysis as follows:
    “Conclusion:
    Discuss until RAN1#86 to define simple UE energy modelling approach for NR mMTC radio access energy efficiency analysis which is not specific to any particular radio access solution (contact: Karri Ranta-aho)”
The battery models used will impact NR design and evaluation, in terms of
  maximum transmit power
    Processing gain
    eNodeB receiver dynamic range
  waveform design (e.g. PAPR properties of the waveform)
  duty cycles / DRX design
  relay support for wearables and meters
  signalling overheads
  power control mechanisms

## Slide 3: Proposal 1
Characteristic | Battery model A
Nominal voltage | 3.6V
Nominal battery capability | 5Wh (ambient temperature)
Self-discharge rate | 3% per year
Discharge rate capacity backoff | Peukert’s Law (k=1.1)
Capture the following battery models for NR mMTC evaluations in Annex A of TR38.912
Characteristic | Battery model B (small form-factor batteries, e.g. coin cell) | Battery Model C (rechargeable)
Nominal voltage | 3.0V | 3.6V
Nominal capacity | 225mAh (ambient temperature) | 200mAh (ambient temperature)
Maximum continuous current | 3mA | 100mA
Pulse capability | 15mA | 100mA
Battery model B and C (for primary/rechargeable batteries, typical applications: small wearables)
Battery model A (utility meters)

## Slide 4: Proposal 2
Traffic Model | Traffic Model Description
Mobile autonomous reports (MAR) | Pareto distribution with shape parameter alpha = 2.5 and minimum application payload size = MO 20 bytes with a cut off of MO 200 bytes i.e. payloads higher than MO 200 bytes are assumed to be 200 bytes. Periodic inter-arrival time: 1 day (40%), 2 hours (40%), 1 hour (15%), and 30 minutes (5%)
Network Command | Same as MAR but MT messages
Wearable | MT 100 bytes + 20 byte ACK. 1 message per 2 hours.
Precision Tracking | MO 100 bytes + 20 byte ACK. 1 message per minute.
Real-time data | MO 100 bytes + MT 100 bytes every 40ms.
Capture these traffic models for mMTC evaluations in Annex A of TR38.912
Timing is uniformly distributed

## Slide 5: Proposal 3
Traffic Model | Battery model | Battery life | MCL | Latency
Mobile autonomous reports | A | 15 years | 164dB | 10 sec
Network Command | A | 15 years | 164dB | 10 sec
Wearable | B | 1 year | 144dB | 5 sec
 | C | 2 weeks | 144dB | 5 sec
Precision tracking | C | 24 hours | 144dB | 100 ms
Real time data | C | 1 hour | 144dB | 40 ms
The traffic models in the following table are studied with the associated battery model and KPI goals
Traffic Model | % UEs | Capacity
Mobile autonomous reports | 50 | 1 M per km^2
Network Command | 20 | 
Wearable | 22.5 | 
Precision tracking | 2 | 
Real time data | 0.5 |