## Slide 1
Way Forward on RB allocation for mixed numerologies
ZTE, ZTE Microelectronics, Ericsson, Qualcomm, Nokia, Alcatel-Lucent Shanghai Bell, Panasonic
R1-168140
3GPP TSG RAN WG1 #86
Gothenborg, Sweden, 22th – 26th August 2016
Agenda item 8.1.3.1

## Slide 2
Working assumption
  RAN1 concludes on alternative 1 (15 kHz) as the baseline design assumption for the NR numerology
  RAN1 concludes on scale factors N =2n for subcarrier spacing as the baseline design assumption for the NR numerology
Agreements:
PRB definition where the number of subcarriers per PRB is the same for all numerologies is supported
  Examples of the number of subcarriers per PRB for NR study are 12, 10, 16
  Additional PRB definition with the different number of subcarriers is not precluded
For subcarrier spacing of 2n * 15kHz, subcarriers are mapped on the subset/superset of those for subcarrier spacing of 15kHz in a nested manner in the frequency domain
Background

## Slide 3: Proposal
In one carrier,
  RBs for different numerologies are located on a fixed grid
  For subcarrier spacing of 2n * 15kHz, the RB grids are defined as the subset/superset of the RB grid for subcarrier spacing of 15kHz in a nested manner in the frequency domain